## Slide 1
Introduction to Modern Controls
Modeling of Dynamic Systems
Modeling

## Slide 2: Why modeling?
Modeling of physical systems:
a vital component of modern engineering
often consists of complex coupled differential equations
only when we have good understanding of a system can we optimally control it:
▶ can simulate and predict actual system response, and
▶ design model-based controllers
Modeling

## Slide 3: Two general approaches of modeling
based on physics:
▶ using fundamental engineering principles such as Newton’s laws, energy conservation, etc
based on measurement data:
▶ using input-output response of the system
▶ a field itself known as system identification
Modeling

## Slide 4
often the tools are combined in practice
Modeling

## Slide 5: Example: Mass spring damper
position: y(t)
m
k
b
u = F
Newton’s second law gives
m¨y (t) + by˙ (t) + ky (t) = u (t) , y(0) = y0, y˙(0) = y˙0
modeled as a second-order ODE with input u(t) and output y(t)
Modeling

## Slide 6: Example: HDD
Spindle
Head
Actuator Arm
Actuator Axis
Actuator
Power Connector
Jumper Block
Platter
IDE Connector
Newton’s second law for rotation
letting θ :=output and τ :=input yields
J
θ¨ = α = 1 τ
Modeling

## Slide 7: Example: HDD
Spindle
Head
Actuator Arm
Actuator Axis
Actuator
IDE Connector
Power Connector
Jumper Block
Platter
θ¨ = α = 1 τ ⇔ Θ(s) = 1 T(s)
J Js2
with damping:
n
θ¨ + 2ζωnθ˙ + ω2θ = κτ ⇔ Θ(s) =
κ
s2 + 2ζωns + ωn2
T(s)
with multiple modes:
i
s2 + 2ζiωis + ω2
i
θ¨i + 2ζiωiθ˙i + ω2θi = κiτ ⇔ Θi(s) = κi T(s)
Modeling

## Slide 8: Example: HDD
Spindle
Head
Actuator Arm
Actuator Axis
Actuator
IDE Connector
Power Connector
Jumper Block
Platter
i
s2 + 2ζiωis + ω2
i
θ¨i + 2ζiωiθ˙i + ω2θi = κiτ ⇔ Θi(s) = κi T(s)
final model:
Modeling

## Slide 9
import numpy as np
import matplotlib.pyplot as plt from scipy import signal import control as ct
num_sector = 420 # Number of sector num_rpm = 7200 # Number of RPM Kp_vcm = 3.7976e+07 # VCM gain
omega_vcm = np.array([0, 5300, 6100, 6500, 8050, 9600, 14800, 17400,
21000, 26000, 26600, 29000, 32200, 38300, 43300,
'→ 44800]) * 2 * np.pi
kappa_vcm = np.array([1, -1.0, +0.1, -0.1, 0.04, -0.7, -
0.2, -1.0, +3.0, -3.2, 2.1, -1.5, +2.0, -0.2,
'→ +0.3, -0.5])
zeta_vcm = np.array([0, 0.02, 0.04, 0.02, 0.01, 0.03, 0.01,
0.02, 0.02, 0.012, 0.007, 0.01, 0.03, 0.01, 0.01,
'→ 0.01])
Sys_Pc_vcm_c1 = ct.TransferFunction([], [1]) # Create an empty
'→ transfer function
for i in range(len(omega_vcm)):
Sys_Pc_vcm_c1 = Sys_Pc_vcm_c1 + ct.TransferFunction(np.array(
[0, 0, kappa_vcm[i]]) * Kp_vcm, np.array([1, 2 * zeta_vcm[i] *
'→ omega_vcm[i], (omega_vcm[i]) ** 2]))
Modeling

## Slide 10
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 11
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 12
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 13
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 14
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 15
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 16
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 17
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 18
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 19
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 20
101
102
103
104
50
0
50
100
Gain [dB]
Pcv
101
102
104
103
Frequency [Hz]
0
90
180
270
360
Phase [deg.]
Modeling

## Slide 21: Models of continuous-time systems
modeled as differential equations:
position: y(t)
m
k
b
u = F
Actuator
IDE Connector
Power Connector
Jumper Block
m¨y (t) + by˙ (t) + ky (t) = u (t) , y(0) = y0, y˙(0) = y˙0
Spindle Head
Platter
Actuator Arm
Actuator Axis
i
s2 + 2ζiωis + ω2
i
θ¨i + 2ζiωiθ˙i + ω2θi = κiτ ⇔ Θi(s) = κi T(s)
Modeling

## Slide 22: Models of continuous-time systems
General continuous-time systems:
with the initial conditions y(0
0
(n)
(n)
0
) = y , . . . , y (0) = y .
Modeling

## Slide 23: Models of discrete-time systems
General discrete-time systems
inputs and outputs defined at discrete time instances k = 1, 2, . . .
described by ordinary difference equations in the form of
y(k)+an−1y(k−1)+· · ·+a0y(k−n) = bmu(k+m−n)+· · ·+b0u(k−n)
Example: bank statements
x(k + 1) = (1 + ρ)x(k) + u(k), x(0) = x0
k – month counter; ρ – interest rate; x(k) – wealth at the beginning of month k; u(k) – money saved at the end of month k; x0 – initial wealth in account
Modeling

## Slide 24: Model properties: static v.s. dynamic, causal v.s. acausal
u
M
y
Model M is said to be
memoryless or static if y(t) depends only on u(t)
dynamic (has memory) if y at time t depends on input values at other times
causal if y(t) depends on u(τ ) for τ ≤ t
strictly causal if y(t) depends on u(τ ) for τ < t, e.g.: y(t) = u(t − 10)
Modeling
e.g.: , ,

## Slide 25: Linearity and time-invariance
The system M is called
linear if satisfying the superposition property:
M(α1u1(t) + α2u2(t)) = α1M(u1(t)) + α2M(u2(t))
for any input signals u1(t) and u2(t), and any real numbers α1 and α2 time-invariant if its properties do not change with respect to time e.g., y˙(t) = Ay(t) + Bu(t) is linear and time-invariant
y˙(t) = 2y(t) − sin(y(t))u(t) is nonlinear, yet time-invariant
y˙(t) = 2y(t) − t sin(y(t))u(t) is time-varying
assuming the same initial conditions, if we shift u(t) by a constant time interval, i.e., consider M(u(t + τ0)), then M is time-invariant if the output M(u(t + τ0)) = y(t + τ0)
Modeling

## Slide 26
George Box
“All Models are Wrong, but Some are Useful”
statistical models always fall short of the complexities of reality but can still be useful nonetheless
a dynamic system may simply be too complex (consider the neural system of human brains)
or there are inevitable hardware uncertainties such as the fatigue of gears or bearings in a car
Modeling

## Slide 27: Example (HDDs under perturbation)
temperature influence manufacturing variations but, control works!
103
104
Frequency [Hz]
-80
-60
0
-20
-40
Gain [dB]
Pcv
103
104
Frequency [Hz]
-90
-180
-270
-360
0
Phase [deg.]
Modeling

## Slide 28: Example (HDDs under perturbation)
101
102 103
Frequency [Hz]
104
-200
-180
-160
-140
-120
-100
-80
-60
Amplitude [dB]
Amplitude spectrum of yc
Case 1
Case 2
Case 3
Case 4
Case 5
Case 6
Case 7
Case 8
Case 9
103
104
Frequency [Hz]
-80
-60
-40
-20
0
Gain [dB]
Pcv
103
104
Frequency [Hz]
-360
-270
-180
-90
0
Phase [deg.]
Modeling

## Slide 29: Example (HDDs under perturbation)
0 200
400
600
800
1000
Time [ms]
-15
-10
-5
0
5
10
15
Amplitude [% of Track width]
yc
Case 1
Case 2
Case 3
Case 4
Case 5
Case 6
Case 7
Case 8
Case 9
103
104
Frequency [Hz]
-80
-60
-40
-20
0
Gain [dB]
Pcv
103
104
Frequency [Hz]
-360
-270
-180
-90
0
Phase [deg.]
Modeling

## Slide 30: Example (HDDs under perturbation)
103
104
Frequency [Hz]
0
-20
-40
-60
-80
Gain [dB]
Pcv
103
104
Frequency [Hz]
0
-90
-180
-270
-360
Phase [deg.]
Modeling