## Slide 1: Observer and Observer State Feedback
Linear Systems
Observers and Observer State FB

## Slide 2: Introduction
▶ full state feedback is usually not available
▶ the state estimation problem
▶ deterministic case: observer design
▶ stochastic case: the most frequent option is Kalman filter
Observers and Observer State FB
2 / 27

## Slide 3: Open-loop observer
d dt
x (t) = Ax (t) + Bu(t), x (k + 1) = Ax (k) + Bu(k)
▶ conceptually simplest scheme to estimate x :
d dt
xˆ(t) = Axˆ(t) + Bu(t), xˆ(k + 1) = Axˆ(k) + Bu(k)
e.g.
with a best guess of initial estimate xˆ(0) = 0.
▶ error dynamics: e = x − xˆ:
(t) = Ae(t), e(k + 1) = Ae(k), e(0) = x0 − xˆ(0)
▶ sensitive to input disturbances
▶ if A is not Hurwitz/Schur stable, the error diverges
▶ open-loop observers look simple but do not work in practice
Observers and Observer State FB
3 / 27

## Slide 4: Luenberger (closed-loop) observer concept
▶ given system dynamics
= Ax + Bu, x (0) = x0, A ∈ Rn×n, B ∈ Rn×r
y = Cx, y ∈ Rm×n
▶ in contrast to open-loop observers, the Luenberger observer adds correction based on output differences
Observers and Observer State FB
4 / 27

## Slide 5: Luenberger (closed-loop) observer algorithm
observer concept
plant:
= Ax + Bu, x (0) = x0 y = Cx
▶ observer realization:
= Axˆ + Bu + L (y − yˆ) = Axˆ + Bu + L (y − C xˆ) , xˆ(0) = 0
= (A − LC ) xˆ + Ly + Bu
Observers and Observer State FB
5 / 27

## Slide 6: Luenberger (closed-loop) observer error dynamics
▶ system dynamics
= Ax + Bu, x (0) = x0, A ∈ Rn×n, B ∈ Rn×r
y = Cx, y ∈ Rm×n
▶ Luenberger observer with correction:
= Axˆ + Bu + L (y − yˆ) = Axˆ + Bu + L (y − C xˆ) , xˆ(0) = 0
= (A − LC ) xˆ + Ly + Bu
▶ error dynamics: e = x − xˆ:
= Ae − LCe = (A − LC )e, e(0) = x (0)
▶ if all eigenvalues of A − LC are on the left half plane, then the error dynamics can be made asymptotically stable
Observers and Observer State FB
6 / 27

## Slide 7: Luenberger (closed-loop) observer
Theorem
If (A, C ) is an observable pair, then all the eigenvalues of A − LC can be arbitrarily assigned, provided that they are symmetric with respct to the real axis of the complex plane.
▶ we show the SISO case when A and C are in observable canonical form (if not, a similarity transform can help out):
Observers and Observer State FB
7 / 27

## Slide 8: Observer eigenvalue placement: o.c.f.
▶ Luenberger observer with correction:
= Axˆ + Bu + L (y − yˆ) = Axˆ + Bu + L (y − C xˆ) , xˆ(0) = 0
= (A − LC ) xˆ + Ly + Bu
▶ Goal: place eigenvalues of the observer at locations :
Observers and Observer State FB
8 / 27

## Slide 9: Observer eigenvalue placement: o.c.f.
▶ Goal: place eigenvalues of the observer at locations :
▶ Let L = [l0, l1, . . . , ln−1]T . The unique structures of A and C give
Observers and Observer State FB
9 / 27

## Slide 10: Observer eigenvalue placement: o.c.f.
▶ A and A − LC have the same structure:
▶ Recall: det (sI − A) = sn + αn−1sn−1 + + α1s + α0.
▶ Thus
▶ Hence
Observers and Observer State FB
10 / 27

## Slide 11: General observer eigenvalue placement
▶ What if (A, B, C, D) is not in the observable canonical form?
▶ We can transform it to o.c.f. via a similarity transform:
▶ use previous formulas to design L˜ in:
=(Ao − L˜Co ) xˆob + L˜y + Bou (analysis form)
▶ correspondingly in the original state space (via xˆob = Rxˆ):
R= (RAR−1 − L˜CR−1)Rxˆ + L˜y + RBu
(implementation form)
Observers and Observer State FB
11 / 27

## Slide 12: General observer eigenvalue placement
▶ Powerful fact: if system Σ = (A, B, C, D) is observable, then we can arbitrarily place the observer eigenvalues.
Observers and Observer State FB

## Slide 13
Observer design in MATLAB and Python
Observers and Observer State FB
%MATLAB | #Python
A = [0 1;-4 -0.2]; B = [0 1]’; | import control as ct
C = [1 0]; | import numpy as np
sys = ss(A,B,C,0); | A = np.array([[0, 1],[-4, -0.2]])
eig(A) | C = np.array([[1], [0]]).T
L = place(A’,C’,[-2,-3])’ | L = ct.place(A.T,C.T,[-2, -3]).T
eig(A-L*C) | print(L)

## Slide 14
Motor control example
Observers and Observer State FB

## Slide 15
Luenberger observer summary
▶ observer dynamics: = Axˆ + Bu + L (y − C xˆ) , xˆ(0) = 0
▶ block diagram
Observers and Observer State FB

## Slide 16: Luenberger observer summary
▶ system dynamics
= Ax + Bu, x (0) = x0, A ∈ Rn×n, B ∈ Rn×r
y = Cx, y ∈ Rm×1
▶ observer dynamics
= Axˆ + Bu + L (y − C xˆ) , xˆ(0) = 0
= (A − LC ) xˆ + LCx + Bu
▶ augmented system
Observers and Observer State FB
16 / 27

## Slide 17: Luenberger observer summary
▶ augmented system
y = Cx
▶ to see the distribution of eigenvalues, note the error dynamics
= (A − LC )e ⇒
⇒eigenvalues are separated into: λ (A) and observer eigenvalues
▶
underlying similarity transform:
Observers and Observer State FB
17 / 27

## Slide 18: Discrete-time observers: Introduction
▶ full state feedback is usually not available
▶ often observers are implemented in the discrete-time domain
▶ the discrete-time observer design
▶ basic form: analogous to the continuous-time Luenberger observer
▶ predict and correct form:
▶ direct DT design
▶ leverages discrete-time signal properties
Observers and Observer State FB
18 / 27

## Slide 19: Discrete-time full state observer
▶ standard discrete-time observer:
x (k + 1) = Ax (k) + Bu (k)
xˆ(k + 1) = Axˆ(k) + Bu (k) + L (y (k) − C xˆ(k))
y (k) = Cx (k)
▶ error dynamics:e (k) = x (k) − xˆ(k),
e (k + 1) = Ae (k) − LCe (k)
▶ overall dynamics
▶ Powerful fact: the error dynamics can be arbitrarily assigned if the system is observable.
Observers and Observer State FB
19 / 27
x (k + 1)
e (k + 1)
=
A 0
0 A − LC
+
B
0
u (k)
y (k + 1) = [C, 0]
x (k)
e (k)
x (k + 1)
e (k + 1)

## Slide 20: DT full state observer with predictor
▶ motivation: xˆ(k + 1) = Axˆ(k) + Bu (k) + L (y (k) − C xˆ(k))
doesn’t use most recent measurement y (k + 1) = Cx (k + 1)
▶ discrete-time observer with predictor:
predictor: xˆ(k + 1|k) = A xˆ(k|k) + Bu (k)
corrector: xˆ(k + 1|k + 1) = xˆ(k + 1|k) + L (y (k + 1) − C xˆ(k + 1|k))
▶ xˆ(k|k): estimate of x (k) based on measurements up to time k
▶ xˆ(k|k − 1): estimate based on measurements up to time k − 1
▶ e(k) ≜ x (k) − xˆ(k|k): estimation error
▶ error dynamics
xˆ(k + 1|k + 1) = (I − LC ) xˆ(k + 1|k) + Ly (k + 1)
= (I − LC ) A xˆ(k|k) + (I − LC ) Bu (k) + Ly (k + 1)
⇒ e (k + 1) = x (k + 1) − Ly (k + 1) − (I − LC )A xˆ(k|k) − (I − LC )Bu(k)
= (A − LCA) e (k)
Observers and Observer State FB
20 / 27

## Slide 21: DT full state observer with predictor
▶ the error dynamics can be arbitrarily assigned if the pair
(A, C˜)= (A, CA) is observable
▶ observability matrix
▶ if A is invertible, then Q˜d has the same rank as Qd
▶ (A, C˜)is observable if (A, C ) is observable and A is nonsingular (guaranteed if discretized from a CT system)
Observers and Observer State FB
21 / 27

## Slide 22: Example
Observers and Observer State FB
y (k) = x1(k). Place all eigenvalues of an observer with predictor
at the origin.
det (A − LCA − λI ) = ((l1 − 1) a2 − λ) (l2 + λ) λ +
(1 − l1) (l3aa − a0) + l3 ((l1 − 1) a2 − λ) + λ (1 − l1) (l2a2 − a1)
roots must be all 0 ⇒l1 = 1, l2 = l3 = 0.

## Slide 23: 1. Concepts
Continuous-time Luenberger observer
Discrete-time observers DT full state observer
DT full state observer with predictor
Observer state feedback
Observers and Observer State FB

## Slide 24: Observer state feedback
given system dynamics:
= Ax + Bu y = Cx
▶ state feedback control: arbitrary eigenvalue assignment if system controllable
▶ observer design: arbitrary observer eigenvalue assignment for state estimation if system observable
▶ when full states are not available, what’s the performance if we combine both?
u = −K xˆ + v
Observers and Observer State FB
24 / 27

## Slide 25: Closed-loop dynamics
▶ full closed-loop system
= Ax + Bu y = Cx
= Axˆ + Bu + L (y − C xˆ)
u = −K xˆ + v
▶
using again similarity transform
Observers and Observer State FB
25 / 27
⇒
gives

## Slide 26
Block diagram
▶ = Axˆ + Bu + L (y − C xˆ), u = −K xˆ + v
Observers and Observer State FB

## Slide 27: The separation theorem
▶ closed-loop dynamics
▶ powerful result: separation theorem: closed-loop eigenvalues consist of
▶ eigenvalues of A − BK from the state feedback control design
▶ eigenvalues of A − LC from the observer design
▶ can design K and L separately based on discussed tools
▶ if system is controllable and observable, we can arbitrarily assign the closed-loop eigenvalues
▶ rule of thumb: assign observer dynamics to be faster than state-feedback dynamics
Observers and Observer State FB
27 / 27