## Slide 1: Controllable and Observable Subspaces Kalman Canonical Decomposition
Linear Systems
Kalman decomposition

## Slide 2
Controllable subspace
Observable subspace
Separating the uncontrollable subspace Discrete-time version
Continuous-time version Stabilizability
Separating the unobservable subspace Discrete-time version
Detectability Continuous-time version
Transfer-function perspective
Kalman decomposition
Kalman decomposition

## Slide 3: Controllable subspace: Introduction
Example
1
x (k + 1) = x1(k) + u(k)
x2(k + 1) = 0
1
x (k + 1) = x1(k) + x2(k) + u(k)
x2(k + 1) = x2(k)
▶ there exists controllable and uncontrollable states: x1
controllable and x2 uncontrollable
▶ how to compute the dimensions of the two for general systems?
▶ how to separate them?
Kalman decomposition

## Slide 4: Controllable subspace: Assumptions
Consider an uncontrollable LTI system
x (k + 1) = Ax (k) + Bu (k) , A ∈ Rn×n
y (k) = Cx (k) + Du (k)
Let the controllability matrix
P = [B, AB, A2B, . . . , An−1B]
have rank n1 < n.
Kalman decomposition

## Slide 5: Controllable subspace
▶ The controllable subspace χC is the set of all vectors x ∈ Rn
that can be reached from the origin.
▶ From
Kalman decomposition
χC is the range space of P: χC = (P)

## Slide 6
Controllable subspace
Observable subspace
Separating the uncontrollable subspace Discrete-time version
Continuous-time version Stabilizability
Separating the unobservable subspace Discrete-time version
Detectability Continuous-time version
Transfer-function perspective
Kalman decomposition
Kalman decomposition

## Slide 7: Observable subspace: Introduction
Example
▶ exists observable and unobservable states: x1 observable and x2
unobservable
▶ how to separate the two?
▶ how to separate controllable but observable states, controllable but unobservable states, etc?
Kalman decomposition
x2(k + 1)
y (k)
x1(k + 1) = x1(k) + u(k) = x1(k) + x2(k)
= x1(k)

## Slide 8: Observable subspace: Assumptions
Consider an unobservable LTI system
x (k + 1) = Ax (k) + Bu (k) , A ∈ Rn×n
y (k) = Cx (k) + Du (k)
Let the observability matrix
have rank n2 < n.
Kalman decomposition

## Slide 9: Unobservable subspace
▶ The unobservable subspace χuo is the set of all nonzero initial conditions x (0) ∈ Rn that produce a zero free response.
▶ From
Kalman decomposition
χuo is the null space of Q: χuo = (Q)

## Slide 10
Controllable subspace
Observable subspace
Separating the uncontrollable subspace Discrete-time version
Continuous-time version Stabilizability
Separating the unobservable subspace Discrete-time version
Detectability Continuous-time version
Transfer-function perspective
Kalman decomposition
Kalman decomposition

## Slide 11: Separating the uncontrollable subspace
▶ recall 1: similarity transform x = Mx∗ preserves controllability
⇒
∗ −1 ∗ −1
1) = M AMx (k) + M Bu (k)
x (k + 1) = Ax (k) + Bu (k) x (k +
y (k) = Cx (k) + Du (k) y (k) = CMx∗ (k) + Du (k)
▶ recall 2: the uncontrollable system structure at introduction
▶ decoupled structure for generalized systems
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
[
y (k) = C
c
¯ C¯
uc
x¯c (k)
x¯uc (k)
x¯c (k)
x¯uc (k)
+ Du(k)
x¯uc impacted by neither u nor x¯c .
Kalman decomposition
11 / 31
x1(k + 1) = x1(k) + x2(k) + u(k)
x2(k + 1) = x2(k)
]

## Slide 12: Theorem (Kalman canonical form (controllability))
Let x ∈ Rn, x (k + 1) = Ax (k) + Bu(k), y (k) = Cx (k) + Du(k) be
uncontrollable with rank of the controllability matrix,
rank (P) = n < n. Let M = M
1 c uc
[ ]
M , where
Mc = [m1, . . . , mn1 ] consists of n1 linearly independent columns of P, and Muc = [mn1+1, . . . , mn] are added columns to complete the basis and yield a nonsingular M. Then x = Mx¯ transforms the system equation to
Furthermore, (A¯c , B¯c ) is controllable, and
C (zI − A)−1B + D = C¯c (zI − A¯c )−1B¯c + D
Kalman decomposition
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
[
y (k) = C
c
¯ C¯
uc
x¯c (k)
x¯uc (k)
x¯c (k)
x¯uc (k)
+ Du(k)
]

## Slide 13: Theorem (Kalman canonical form (controllability))
M−1B
intuition: the “B” matrix after transformation
▶ columns of B ∈ column space of P, which is equivalent to
(Mc )
▶ columns of Muc and Mc are linearly independent ⇒ columns of
B ∈/ (Muc )
▶ thus
Kalman decomposition
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
x¯c (k)
x¯uc (k)

## Slide 14: Theorem (Kalman canonical form (controllability))
M−1AM
intuition: the “A” matrix after transformation
▶ the range space of Mc is “A-invariant”:
where columns of AnB ∈ (P) = (Mc ) (∵ Cayley Halmilton Thm)
▶ i.e., AMc = Mc A¯c for some A¯c ⇒
Kalman decomposition
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
x¯c (k)
x¯uc (k)
columns of AM ∈ AB, A B, . . . , A B ∈ (M )
2 n
{ }
c c

## Slide 15: Theorem (Kalman canonical form (controllability))
(A¯c , B¯c ) is controllable
▶ controllability matrix after similarity transform
▶ similarity transform does not change controllability ⇒ rank(P¯) = rank(P) = n1
▶ thus rank(P¯c ) = n1 ⇒(A¯c , B¯c ) is controllable
Kalman decomposition
M−1AM
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
x¯c (k)
x¯uc (k)
M−1B

## Slide 16: Theorem (Kalman canonical form (controllability))
C (zI − A)−1B + D = C¯c (zI − A¯c )−1B¯c + D
we can check that
Kalman decomposition
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
[
y (k) = C
c
¯ C¯
uc
x¯c (k)
x¯uc (k)
x¯c (k)
x¯uc (k)
+ Du(k)
]

## Slide 17: Matlab commands
[
x = Mx¯ where M = M
M
c uc
]
▶ Mc = [m1, . . . , mn1 ] consists of all the linearly independent columns of P: Mc = orth(P)
▶ Muc = [mn1+1, . . . , mn] are added columns to complete the basis and yield a nonsingular M
▶ from linear algebra: the orthogonal complement of the range space of P is the null space of PT :
▶ hence Muc = null(P’) (the transpose is important here)
Kalman decomposition
M−1AM
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
x¯c (k)
x¯uc (k)
M−1B

## Slide 18: The techniques apply to CT systems
Theorem (Kalman canonical form (controllability))
Let a n-dimensional state-space system = Ax + Bu, y = Cx + Du
be uncontrollable with the rank of the controllability matrix
rank (P) = n < n. Let M = M
1 c uc
[ ]
M where
Mc = [m1, . . . , mn1 ] consists of n1 linearly independent columns of P, Muc = [mn1+1, . . . , mn] are added columns to complete the basis for Rn and yield a nonsingular M. Then the similarity transformation
x = Mx¯ transforms the system equation to
Kalman decomposition
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u
[
y = C
c
¯ C¯
uc
]
x¯c
x¯uc
+ Du
x¯c
x¯uc
x¯c
x¯uc

## Slide 19: Example
−1 1 − k − k
P = 0 k1
0 k2
0 , B = M B =
, M = 0
−1 1/k1
k1 0 , M = 0 1/k1 0
0 k2 1 0 −k2/k1 1
v
m
k
1
Fk2
F =
−b/m −1/m −1/m
k1 k2
0
0
0
0
v
m
k
1
Fk2
F +
1/m 0
0
F
Let m = 1, b = 1
1
1 2
−k1
−k2
1
0
−1
0
¯
−1
A = M AM =
0
0
1
− (k1 + k2)
1 −1
0
−1
0
0 0
1
1
Kalman decomposition

## Slide 20: Stabilizability
The system is stabilizable if
▶ all its unstable modes, if any, are controllable
▶ i.e., the uncontrollable modes are stable (A¯uc is Schur, namely, all eigenvalues are in the unit circle)
Kalman decomposition
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
[
y (k) = C
c
¯ C¯
uc
x¯c (k)
x¯uc (k)
x¯c (k)
x¯uc (k)
+ Du(k)
]

## Slide 21
Controllable subspace
Observable subspace
Separating the uncontrollable subspace Discrete-time version
Continuous-time version Stabilizability
Separating the unobservable subspace Discrete-time version
Detectability Continuous-time version
Transfer-function perspective
Kalman decomposition
Kalman decomposition

## Slide 22: Separating the unobservable subspace
▶ recall 1: similarity transform x = O−1x∗ preserves observability
▶ an unobservable system structure
▶ decoupled structure for generalized systems
Kalman decomposition
x (k + 1) = Ax (k) + Bu (k)
y (k) = Cx (k) + Du (k)
⇒
x∗ (k + 1) = OAO−1x∗ (k) + OBu (k)
y (k) = CO−1x∗ (k) + Du (k)
y (k)
1
x (k +1)
x2(k +1 )
= x1(k) + u(k)
= x1(k) + x2(k)
= x1(k)
x¯o (k + 1)
x¯uo (k + 1)
=
¯
A
o
A¯21
0 x¯o (k)
x¯uo (k)
B¯o
B¯uo
u(k)
[
¯
y (k) = C
o
x¯o (k)
x¯uo (k)
+ Du(k)
0 ]
+
the “observed” x¯o doesn’t reflect

## Slide 23: Theorem (Kalman canonical form (observability))
Let x ∈ Rn, x (k + 1) = Ax (k) + Bu(k), y (k) = Cx (k) + Du(k) be unobservable with rank of the observability matrix,
rank (Q) = n2 < n. Let O =
Oo Ouo
o
where O consists of n2
uo
linearly independent rows of Q, and O = o
T
T
n1+1 n
[ ]
T
, . . . , o are
added rows to complete the basis and yield a nonsingular O. Then
x¯ = Ox transforms the system equation to
Furthermore, (A¯o , O¯o ) is observable, and
C (zI − A)−1B + D = C¯o (zI − A¯o )−1B¯o + D
Kalman decomposition
x¯o (k + 1)
x¯uo (k + 1)
=
¯
A
o
A¯21
0 x¯o (k)
x¯uo (k)
B¯o
B¯uo
u(k)
[
¯
y (k) = C
o
x¯o (k)
x¯uo (k)
+ Du(k)
0 ]
+

## Slide 24: Theorem (Kalman canonical form)
Case for observability
v.s. case for controllability
Intuition: duality between controllability and observability
(A, B) unconrollable ⇔ (AT , BT ) unobservable
Kalman decomposition
x¯o (k + 1)
x¯uo (k + 1)
=
¯
A
o
A¯21
0 x¯o (k)
x¯uo (k)
B¯o
B¯uo
u(k)
[
¯
y (k) = C
o
x¯o (k)
x¯uo (k)
+ Du(k)
0 ]
+
x¯c (k + 1)
x¯uc (k + 1)
=
A
c
¯ ¯
A
12
0
A¯uc
+
¯
B
c
0
u(k)
[
y (k) = C
c
¯ C¯
uc
x¯c (k)
x¯uc (k)
x¯c (k)
x¯uc (k)
+ Du(k)
]

## Slide 25: Detectability
The system is detectable if
▶ all its unstable modes, if any, are observable
▶ i.e., the unobservable modes are stable (A¯uo is Schur)
Kalman decomposition
x¯o (k + 1)
x¯uo (k + 1)
=
¯
A
o
A¯21
0 x¯o (k)
x¯uo (k)
B¯o
B¯uo
u(k)
[
¯
y (k) = C
o
x¯o (k)
x¯uo (k)
+ Du(k)
0 ]
+

## Slide 26: Continuout-time version
Theorem (Kalman canonical form (observability))
Let a n-dimensional state-space system = Ax + Bu, y = Cx + Du
be unobservable with the rank of the observability matrix rank (Q) = n2 < n. Then there exists similarity transform x¯ = Ox that transforms the system equation to
Furthermore, (A¯o , C¯o ) is observable, and
C (sI − A)−1B + D = C¯o (sI − A¯o )−1B¯o + D.
Kalman decomposition

## Slide 27
Controllable subspace
Observable subspace
Separating the uncontrollable subspace Discrete-time version
Continuous-time version Stabilizability
Separating the unobservable subspace Discrete-time version
Detectability Continuous-time version
Transfer-function perspective
Kalman decomposition
Kalman decomposition

## Slide 28: Transfer-function perspective
G (z ) = C (zI − A)−1B + D = , A(z ) = det (zI − A) order : n
uncontrollable system: C (zI − A)−1B + D = C¯c (zI − A¯c )−1B¯c + D
unobservable system: C (zI − A)−1B + D = C¯o (zI − A¯o )−1B¯o + D
where A ∈ Rn×n, A¯c ∈ Rn1×n1 , A¯o ∈ Rn2×n2
▶ Order reduction exists
▶ ⇒ A(z ) and B(z ) are not co-prime | pole-zero cancellation exists
▶
same applies to unobservable systems
Kalman decomposition
order:

## Slide 29: Example
Consider
x
1
x2
=
1
0 1 x
−2 −3 x2
+
0
1
u
y =[c1 1
]
x
1
x2
▶ The transfer function is
▶ System is in controllable canonical form and is controllable.
▶ observability matrix
Q =
c1 1
−2 c1 − 3
, det Q = (c1 − 1) (c1 − 2)
⇒ unobservable if c1 = 1 or 2
Kalman decomposition

## Slide 30
Controllable subspace
Observable subspace
Separating the uncontrollable subspace Discrete-time version
Continuous-time version Stabilizability
Separating the unobservable subspace Discrete-time version
Detectability Continuous-time version
Transfer-function perspective
6. Kalman decomposition
Kalman decomposition
30 / 31

## Slide 31: Kalman decomposition
an extended example:
A =
A11 | 0 | A13 | 0
A21 | A22 | A23 | A24
0 0 | 0 0 | A33 A43 | 0 A44
, B =
B
2
0
0
0 ]
C = [ C1 0 C3
▶ Aij , Ci and Bi are nonzero
▶ The A11 mode is controllable and observable. The A22 mode is controllable but not observable. The A33 mode is not controllable but observable. The A44 mode is not controllable
and not observable.
Kalman decomposition
31 / 31
B1