## Slide 1
Introduction to Modern Controls
State-Space Introduction

## Slide 2: Why state space?
static/memoryless system: present output depends only on its present input: y(k) = f(u(k))
dynamic system: present output depends on past and its present input,
▶ e.g., y(k) = f(u(k), u(k − 1), . . . , u(k − n), . . . )
▶ described by differential or difference equations, or have time delays
how much information from the past is needed?
State-Space Introduction

## Slide 3: The concept of states of a dynamic system
the state x(t) is the information you need at time t that together with future values of the input, will let you compute future values of the output y
loosely speaking:
▶ the “aggregated effect of past inputs”
▶ the necessary “memory” that the dynamic system keeps at each time instance
State-Space Introduction

## Slide 4: Example
position: y(t)
m
k
b
u = F
to predict the future motion, we need to know
▶ current position and velocity
▶ future force
⇒ states: position and velocity
State-Space Introduction

## Slide 5: The order of a dynamic system
position: y(t)
m
k
b
u = F
the number, n of state variables that is necessary and suﬀicient to uniquely describe the system
for a given dynamic system,
▶ the choice of state variables is not unique
▶ however, its order n is fixed
▶ i.e. you need not more than n but not less than n state variables
State-Space Introduction

## Slide 6: States of a discrete-time system
consider a discrete-time dynamic system:
the state at any instance ko is the minimum set of variables,
x1(ko), x2(ko), ⋯, xn(ko)
that fully describe the system and its response for k ≥ ko to any given set of inputs
loosely speaking, x1(ko), x2(ko), ⋯, xn(ko) defines the system’s memory
State-Space Introduction
u (k)
System
x1,x2,...,xn
y(k)

## Slide 7: Discrete-time state-space description
general case
x(k + 1) = f(x(k), u(k), k)
y(k) = h(x(k), u(k), k)
u(k): input; y(k): output
x(k): state
x(k + 1) = f(·): state Eq
y(k) = h(·): output Eq
linear time-invariant (LTI) case
x(k + 1) = Ax(k) + Bu(k)
y(k) = Cx(k) + Du(k)
Σ(A, B, C, D) denotes a
state-space realization
State-Space Introduction
u (k)
System
x1,x2,...,xn
y(k)
also written as

## Slide 8: Continuous-time state-space description
general case
dx(t)
= f(x(t), u(t), t)
dt
y(t) = h(x(t), u(t), t)
LTI case
dx(t)
= Ax(t) + Bu(t)
dt
y(t) = Cx(t) + Du(t)
State-Space Introduction
u (t)
System
x1,x2,...,xn
y(t)

## Slide 9: Example: mass-spring-damper
position: y(t)
m
k
b
u = F
State-Space Introduction

## Slide 10: Example: mass-spring-damper
position: y(t)
m
k
b
u = F
State-Space Introduction

## Slide 11: Coding a continuous-time state-space system in MATLAB
A = [0,1;-3,-2];
B = [0;1];
C = [2,1];
D = 0;
sys_ss = ss(A,B,C,D)
[yout, T] = step(sys_ss); figure, plot(T, yout)
State-Space Introduction

## Slide 12: Coding a continuous-time state-space system in Python
import control as co
import matplotlib.pyplot as plt import numpy as np
A = np.array([[0,1],[-3,-2]])
B = np.array([[0],[1]])
C = np.array([2,1])
D = np.array([0])
sys_ss = co.ss(A,B,C,D) print(sys_ss)
T,yout = co.step_response(sys_ss)
plt.figure(1,figsize = (6,4)) plt.plot(T,yout) plt.grid(True) plt.ylabel("y")
plt.xlabel("Time (sec)") plt.show()
State-Space Introduction