## Slide 1: Introduction to Modern Controls
Discretization of Continuous-time Transfer-function Models
TF Discretization

## Slide 2: Overview
consider the discrete-time controller implementation scheme
where u[k] and y[k] have the same sampling time
for this note, we use [k] to distinguish DT signals from their CT counter parts
goal: to derive the transfer function from u[k] to y[k]
solution concept: let u[k] be a discrete-time unit impulse (whose Z transform is 1) and obtain the Z transform of y[k]
TF Discretization
u[k]
ZOH
G (s)
y[k]
y(t)
u(t)

## Slide 3: Solution
1 − e−s∆T s
TF Discretization
u[k]
ZOH
G (s)
y[k]
y(t)
u(t)
u[k] is a DT impulse ⇒ after ZOH
u(t) =
1, 0 ≤ t < ∆T
0, otherwise
= 1(t) − 1 t
( − ∆T
) ⇒ U(s) =
hence

## Slide 4: Solution
TF Discretization
u[k]
ZOH
G (s)
y[k]
y(t)
u(t)
sampling y(t) at ∆T and performing Z transform give:

## Slide 5: Solution
TF Discretization
u[k]
ZOH
G (s)
y[k]
y(t)
u(t)
the zero order hold equivalent of is
where is the sampling time

## Slide 6: Example: obtain the ZOH equivalent of
G(s) =
a
s + a
TF Discretization
hence
sampling at gives , whose Z transform is
hence the ZOH equivalent is

## Slide 7: Matlab and Python commands
c2d(G,dt,’zoh’)
s2
e.g., G(s) = 1 and ∆T = 1
% matlab dt = 1;
num = 1;
den = [1,0,0];
G = tf(num,den);
Gd = c2d(G,dt,'zoh');
#Python
import control as ct dt = 1
num = [1]
den = [1,0,0]
G = ct.tf(num,den)
Gd = ct.c2d(G,dt,'zoh') print(Gd)
TF Discretization

## Slide 8
% MATLAB code to generate a single-stage HDD model
num_sector=420; num_rpm=7200;
Ts = 1/(num_rpm/60*num_sector);
% Number of sector
% Number of RPM
% Sampling time
Kp_vcm=3.7976e+07; % VCM gain
omega_vcm=[0, 5300 ,6100 ,6500 ,8050 ,9600 ,14800 ,17400 ,21000 ,26000
'→ ,26600 ,29000 ,32200 ,38300 ,43300 ,44800]*2*pi;
kappa_vcm=[1, -1.0 ,+0.1 ,-0.1 ,0.04 ,-0.7 ,-0.2 ,-1.0 ,+3.0 ,-3.2
'→ ,2.1 ,-1.5 ,+2.0 ,-0.2 ,+0.3 ,-0.5 ];
zeta_vcm =[0, 0.02 ,0.04 ,0.02 ,0.01 ,0.03 ,0.01 ,0.02 ,0.02 ,0.012
'→ ,0.007 ,0.01 ,0.03 ,0.01 ,0.01 ,0.01 ];
Sys_Pc_vcm_c1=0;
for i=1:length(omega_vcm)
Sys_Pc_vcm_c1=Sys_Pc_vcm_c1+tf([0,0,kappa_vcm(i)]*Kp_vcm,[1,
'→ 2*zeta_vcm(i)*omega_vcm(i), (omega_vcm(i))^2]);
end
Sys_Pd_vcm_c1 = c2d(Sys_Pc_vcm_c1,Ts,'zoh') Sys_Pd1_vcm_c1 = c2d(Sys_Pc_vcm_c1,Ts*2,'zoh') Sys_Pd2_vcm_c1 = c2d(Sys_Pc_vcm_c1,Ts/2,'zoh')
TF Discretization
8 / 9

## Slide 9: figure, bodeplot(Sys_Pc_vcm_c1) figure, bodeplot(Sys_Pc_vcm_c1,Sys_Pd2_vcm_c1)
figure, bodeplot(Sys_Pc_vcm_c1,Sys_Pd2_vcm_c1,Sys_Pd_vcm_c1) figure,
'→ bodeplot(Sys_Pc_vcm_c1,Sys_Pd2_vcm_c1,Sys_Pd_vcm_c1,Sys_Pd1_vcm_c1)
101
102
104
103
Frequency [Hz]
100
50
0
-50
Gain [dB]
Pcv
104
103
Frequency [Hz]
0
-90
-180
-270
-360
101 102
Phase [deg.]
TF Discretization
8 / 9

## Slide 10
Magnitude (dB)
50
0
-50
-100
-150
1800
1440
1080
720
360
0
Phase (deg)
Bode Diagram
-360
-720
103
104
105
Frequency (rad/s)
106
107
TF Discretization
8 / 9

## Slide 11
Magnitude (dB)
50
0
-50
-100
-150
1800
1440
1080
720
360
0
Phase (deg)
Bode Diagram
-360
-720
103
104
105
Frequency (rad/s)
106
107
TF Discretization
8 / 9

## Slide 12
Magnitude (dB)
102
103
106
107
100
50
0
-50
-100
-150
1800
1440
1080
720
360
0
-360
-720
Phase (deg)
Bode Diagram
104 105
Frequency (rad/s)
TF Discretization
9 / 9

## Slide 13: Exercise
Find the zero order hold equivalent of G (s) = e−Ls, 2∆T < L < 3∆T, where ∆T is the sampling time.
TF Discretization
9 / 9