## Slide 1: Linear Systems: Stability
Stability

## Slide 2: 1. Definitions in Lyapunov stability analysis
2. Stability of LTI systems: method of eigenvalue/pole locations
Stability

## Slide 3: Finite dimensional vector norms
e.g., 2 (Euclidean) norm:
Let v ∈ Rn. A norm is:
▶ a metric in vector space: a function that assigns a real-valued
length to each vector in a vector space
▶
default in this set of notes:
Stability
3 / 23

## Slide 4: Equilibrium state
For an n-th order unforced system
= f (x, t) , x (t0) = x0
an equilibrium state/point xe is one such that
f (xe, t) = 0, ∀t
▶ the condition must be satisfied by all t ≥ 0
▶ if a system starts at equilibrium state, it stays there
Stability
4 / 23

## Slide 5: Equilibrium state of a linear system
For a linear system
(t) = A(t)x (t), x (t0) = x0
▶ origin xe = 0 is always an equilibrium state
▶ when A(t) is singular, multiple equilibrium states exist
Stability
5 / 23

## Slide 6: Lyapunov’s definition of stability
▶ The equilibrium state 0 of = f (x, t) is stable in the sense of Lyapunov (s.i.L) if for all ϵ > 0, and t0, there exists δ (ϵ, t0) > 0 such that ∥x (t0) ∥2 < δ gives ∥x (t) ∥2 < ϵ for all t ≥ t0
Figure: Stable s.i.L: ∥x (t0) ∥ < δ ⇒ ∥x (t) ∥ < ϵ ∀t ≥ t0.
Stability
6 / 23

## Slide 7: Asymptotic stability
The equilibrium state 0 of = f (x, t) is asymptotically stable if
▶ it is stable in the sense of Lyapunov, and
▶ for all ϵ > 0 and t0, there exists δ (ϵ, t0) > 0 such that
∥x (t0) ∥2 < δ gives x (t) → 0
Figure: Asymptotically stable i.s.L: ∥x (t0) ∥ < δ ⇒ ∥x (t) ∥ → 0.
Stability
7 / 23

## Slide 8: 1. Definitions in Lyapunov stability analysis
2. Stability of LTI systems: method of eigenvalue/pole locations
Stability

## Slide 9: Stability of LTI systems: method of eigenvalue/pole locations
the stability of the equilibrium point 0 for = Ax or
x (k + 1) = Ax (k) can be concluded immediately based on λ (A):
▶ the response eAtx (t0) involves modes such as eλt , teλt , eσt cos ωt, eσt sin ωt
▶ the response Akx (k0) involves modes such as λk , kλk−1, r k cos kθ, r k sin kθ
▶ eσt → 0 if σ < 0; eλt → 0 if λ < 0
▶ λk → 0 if |λ| < 1; r k → 0 if |r | = || = |λ| < 1
Stability
9 / 23

## Slide 10
Stability of the origin for x˙ = Ax
stability λi (A) at 0
unstable Re {λi} > 0 for some λi or Re {λi} ≤ 0 for all λi ’s but for a repeated λm on the imaginary axis with multiplicity m, nullity (A − λmI ) < m (Jordan form)
stable Re {λi} ≤ 0 for all λi ’s and ∀ repeated λm on the i.s.L imaginary axis with multiplicity m, nullity (A − λmI ) = m (diagonal form)
asymptotically Re {λi} < 0 ∀λi (A is then called Hurwitz stable) stable
Stability

## Slide 11: Example (Unstable moving mass)
▶ λ1 = λ2 = 0, m = 2,
▶ i.e., two repeated eigenvalues but needs a generalized
▶
Stability
11 / 23
i
nullity (A − λ I ) = nullity
= 1 < m
eigenvector ⇒ Jordan form after similarity transform
At
verify by checking e =
: t grows unbounded

## Slide 12: Example (Stable in the sense of Lyapunov)
▶ λ1 = λ2 = 0, m = 2,
▶
Stability
12 / 23
At
verify by checking e =
i
nullity (A − λ I ) = nullity
= 2 = m

## Slide 13: Routh-Hurwitz criterion
▶ the Routh Test (by E.J. Routh, in 1877): a simple algebraic procedure to determine how many roots a given polynomial
A(s) = ansn + an−1sn−1 + · · · + a1s + a0
has in the closed right-half complex plane, without the need to explicitly solve for the roots
▶ German mathematician Adolf Hurwitz independently proposed in 1895 to approach the problem from a matrix perspective
▶ popular if stability is the only concern and no details on eigenvalues (e.g., speed of response) are needed
Stability
13 / 23

## Slide 14: Routh-Hurwitz criterion
▶ the asymptotic stability of the equilibrium point 0 for = Ax
can also be concluded based on the Routh-Hurwitz criterion
▶ simply apply the Routh Test to A(s) = det (sI − A)
▶ recap: the poles of transfer function G (s) = C (sI − A)−1 −B1 + D
come from det (sI − A) in computing the inverse (sI − A)
Stability
14 / 23

## Slide 15: The Routh Array
▶ first two rows contain the coefficients of A(s)
▶ third row constructed from the previous two rows via
a c
·
· · ·
·
Stability
15 / 23
b d
x ·
y ·
·
·
·
bc − ad
c
xc − ay
c
·
for A(s) = ansn + an−1sn−1 + · · · + a1s + a0, construct
an−2 an−4 an−6
· · ·
· · ·
an
an−1 an−3 qn−2 qn−4
an−5 an−7 qn−6
· · ·
sn sn−1 sn−2 sn−3
qn−3
qn−5
qn−7
· · ·
.
.
.
.
.
.
s1
s0
. .
x2 x0
x0

## Slide 16: The Routh Array
▶ All roots of A(s) are on the left half s-plane if and only if all elements of the first column of the Routh array are positive.
Stability
16 / 23
for A(s) = ansn + an−1sn−1 + · · · + a1s + a0, construct
an−2 an−4 an−6
· · ·
· · ·
an
an−1 an−3 qn−2 qn−4
an−5 an−7 qn−6
· · ·
sn sn−1 sn−2 sn−3
qn−3
qn−5
qn−7
· · ·
.
.
.
.
.
.
s1
s0
. .
x2 x0
x0

## Slide 17: The Routh Array
Example (A(s) = 2s4 + s3 + 3s2 + 5s + 10)
2 | 3 | 10
1 | 5 | 0
2×5
3 − = −7
s4 s3 s2 s1
5 −
1 1×10
−7
0
s 10
10 | 0
0 | 0
0 | 0
▶ two sign changes in the first column
▶ unstable and two roots in the right half side of s-plane
Stability
17 / 23

## Slide 18: The Routh Array
special cases:
▶ If the 1st element in any one row of Routh’s array is zero, one can replace the zero with a small number ϵ and proceed further.
▶ There are other possible complications, which we will not pursue further. See, e.g. "Automatic Control Systems", by Kuo, 7th ed., pp. 339-340.
Stability
18 / 23

## Slide 19: Stability of the origin for x (k + 1) = f (x (k), k)
▶ stability analysis follows analogously for nonlinear time-varying discrete-time systems of the form
x (k + 1) = f (x (k), k) , x (k0) = x0
▶ equilibrium point xe :
f (xe, k) = xe, ∀k
▶ without loss of generality, 0 is assumed an equilibrium point
Stability
19 / 23

## Slide 20
Stability of the origin for x (k + 1) = Ax (k)
stability λi (A) at 0
unstable ¦λi¦ > 1 for some λi or ¦λi¦ ≤ 1 for all λi ’s but for a repeated λm on the unit circle with multiplicity m, nullity (A − λmI ) < m (Jordan form)
stable ¦λi¦ ≤ 1 for all λi ’s but for any repeated λm on the unit i.s.L circle with multiplicity m, nullity (A − λmI ) = m (diagonal form)
asymptotically ¦λi¦ < 1 ∀λi (such a matrix is called Schur stable) stable
Stability

## Slide 21: Routh-Hurwitz criterion for DT LTI systems
▶ the stability domain |λi| < 1 is a unit disk
▶ Routh array validates stability in the left-half plane
▶ bilinear transformation maps the closed left half s-plane to the closed unit disk in z -plane
Real
Imaginary Imaginary
s-plane z -plane
Real
1
1−s
Bilinear transform
z = 1+s or s = z−1
z +1
−1
Stability
21 / 23

## Slide 22: Routh-Hurwitz criterion for DT LTI systems
▶ Given A(z ) = zn + a1zn−1 + · · · + an, procedures of Routh-Hurwitz test:
▶ apply bilinear transform
▶ apply Routh test to
Stability

## Slide 23: Routh-Hurwitz criterion for DT LTI systems
Example (A(z ) = z 3 + 0.8z 2 + 0.6z + 0.5)
z = 1−s
3
3 2
▶ A∗(s) = A(z )| 1+s (1 − s) = (1 + s) + 0.8 (1 + s) (1 − s) +
0.6 (1 + s) (1 − s)2 + 0.5 (1 − s)3 = 0.3s3 + 3.1s2 + 1.7s + 2.9
▶ Routh array
s3 s2
s 1.7 −
s0
1.7
2.9
= 1.42 0
0
0.3
3.1
0.3×2.9
3.1
2.9
▶ all elements in first column are positive ⇒ roots of A(z ) are all in the unit circle
Stability
23 / 23