## Slide 1: Controllability and Observability
Linear Systems

## Slide 2: Outline
Concepts
DT controllability
Controllability and controllable canonical form Controllability and Lyapunov Eq.
DT observability
Observability and observable canonical form
CT cases
The degrees of controllability and observability
Transforming controllable systems into controllable canonical forms
Transforming observable systems into observable canonical forms
Controllability and Observability

## Slide 3
Recap
General LTI state-space models:
(t) = Ax (t) + Bu (t) or x (k + 1) = Ax (k) + Bu (k)
y = Cx + Du
 | continuous time | discrete time
Lyapunov Eq. | AT P + PA = −Q | AT PA − P = −Q
unique sol. cond. | λi (A) + λj (A) 0 ∀ i , j | ¦λi (A)¦ ¦λj (A)¦ < 1 ∀ i , j
solution | (if A is Hurwitz stable) | (if A is Schur stable)
 | continuous time | discrete time
Lyapunov Eq. | AT P + PA = −Q | AT PA − P = −Q
unique sol. cond. |  | ¦λi (A)¦ ¦λj (A)¦ < 1 ∀ i , j
solution |  | 
Controllability and Observability

## Slide 4: The concept of controllability and observability
Controllability:
▶ inputs do not act directly on the states but via state dynamics:
(t) = Ax (t) + Bu (t) or x (k + 1) = Ax (k) + Bu (k) (1)
▶ can the inputs drive the system to any value in the state space in a finite time?
Observability:
▶ states are not all measured directly but instead impact the output via the output equation:
y = Cx + Du
▶ can we infer fully the initial state from the outputs and the inputs? (can then reveal the full state trajectory through (1))
Controllability and Observability

## Slide 5
In-class demo
Controllability and inverted pendulum on a cart
Controllability and Observability

## Slide 6: The concept of controllability and observability
m
m
u
k
k
b
b
x1, x2
x3, x4
x˙1 = x2 x˙3 = x4
floating force source
▶ assume x (0) = 0
▶ because of symmetry, we always have
x1 (t) = x3 (t) , x2 (t) = x4 (t) , ∀t ≥ 0
▶ state cannot be arbitrarily steered ⇒ uncontrollable
Controllability and Observability

## Slide 7: Controllability definition in discrete time
Definition
A discrete-time linear system x (k + 1) = A(k)x (k) + B(k)u (k) is called controllable at k = 0 if there exists a finite time k1 such that for any initial state x (0) and target state x1, there exists a control sequence {u (k) ; k = 0, 1, . . . , k1} that will transfer the system from x (0) at k = 0 to x1 at k = k1.
Controllability and Observability

## Slide 8: Controllability of LTI systems
n
x (k + 1) = Ax (k) + Bu (k) ⇒ x (n) = A x (0) +
n−1 k=0
A
n−1−k
Bu (k)
n
⇒ x (n) − A x (0) =
▶ given any x (n) and x (0) in Rn,
[u (n − 1) , u (n − 2) , . . . , u (0)]T can be solved if the columns of Pd span Rn
▶ equivalently, system is controllable if Pd has rank n (full row rank)
Controllability and Observability

## Slide 9: Controllability of LTI systems Cont’d
x (k + 1) = Ax (k) + Bu (k) ⇒
n
x (n) − A x (0) =
▶ also, no need to go beyond n: adding AnB, An+1B, . . . does not increase the rank of Pd (Cayley Halmilton Theorem):
1
k
1
x (k )−A x (0
) =
Controllability and Observability

## Slide 10: Theorem (Cayley Halmilton Theorem)
Let A ∈ Rn×n. An is linearly dependent with {I , A, A2, · · · An−1}
Proof.
Consider characteristic polynomial
p (λ) = λn + cn−1λn−1 + · · · + c1λ + c0 = det (λI − A)
= (λ − λ1)m1 . . . (λ − λp )mp
⇒ p (A) = An + cn−1An−1 + · · · + c1A + c0I
= (A − λ1I )m1 . . . (A − λp I )mp , m1 + m2 + · · · + mp = n
Take any eigenvector or generalized eigenvector ti , say, associated to λi :
p (A) ti = (A − λ1I )m1 . . . (A − λp I )mp ti =
(A − λ1I )m1 . . . (A − λp I )mp−1 (λi ti − λpti ) = (λi − λ1)m1 . . . (λi − λp )mp ti = 0
▶ Therefore p (A) [t1, t2, . . . , tn ] = 0.
▶ But T = [t1, t2, . . . , tn ] is invertible. Hence
p (A) = 0 ⇒ An = −c0I − c1A − · · · − cn−1An−1.
Controllability and Observability

## Slide 11
Arthur Cayley: 1821-1895, British mathematician
▶ algebraic theory of curves and surfaces, group theory, linear algebra, graph theory, invariant theory, ...
▶ extraordinarily prolific career: ~1,000 math papers William Hamilton: 1805-1865, Irish mathematician
▶ optics and classical mechanics in physics, dynamics, algebra, quaternions, ...
▶ quaternions: extending complex numbers to higher spatial dimensions: 4D case
i 2 = j2 = k2 = ijk = −1
now used in computer graphics, control theory, orbital mechanics, e.g., spacecraft attitude-control systems
Controllability and Observability

## Slide 12: Theorem (Controllability Theorem)
The n-dimensional r -input LTI system with
x (k + 1) = Ax (k) + Bu (k), A ∈ Rn×n, B ∈ Rn×r is controllable if and only if either one of the following is satisfied
The n × nr controllability matrix
Pd = [B, AB, A2B, . . . , An−1B]
has rank n. (proved in previous three slides)
The controllability gramian
is nonsingular for some finite k1.
Controllability and Observability

## Slide 13: Proof: from controllability matrix to gramian
▶ P
d
is full row rank
▶ a solution to (2) is
[u (n − 1) , u (n − 2
) , . . . , u (0
T T
d
d
d
( )
−1
T n
)] = P P P [x (n) − A x (0
)]
Controllability and Observability
Recall
x (n) − Anx (0) =
(2)
⇒ is nonsingular

## Slide 14: Example
Controllability and Observability
Pd =
⇒ rank(Pd ) = 2 < 3 ⇒uncontrollable
Intuition: x˙1 = λ1x1 is not impacted by the control input at all.

## Slide 15: Example
m
m
u
k
k
b
b
x1, x2
x3, x4
x˙1 = x2 x˙3 = x4
floating force source
Matlab commands: P=ctrb(A,B); rank(P)
Controllability and Observability
0.4 0.4 0 0 x1(k) 0.3
−0.9 −0.07 0
0 0 0.4 0.4 x (k)
0 0 −0.9
1
x (k + 1
)
2
x (k + 1)
x3(k + 1)
x4(k + 1)
=
2
3
−0.07 x4(k)
+
0 x (k) 0.4
0.3
0.4
u (k)
rank (Pd ) = rank
= 2 ⇒ uncontrollable

## Slide 16: Example
Controllability and Observability
⇒ rank(P) = 2
⇒uncontrollable

## Slide 17: Analysis: controllability and controllable canonical form
▶ controllability matrix
has full row rank
▶ system in controllable canonical form is controllable
Controllability and Observability

## Slide 18: Analysis: controllability gramian and Lyapunov Eq.
▶ If A is Schur, k1 can be set to ∞
∞
k=0 Q
which can be solved via the Lyapunov Eq.
AWcd AT − Wcd = −BBT
Controllability and Observability
cd
k1
k=0
k
W = A BB A
T T
( )
k
cd
k
W = A BB A
T T
( )
k

## Slide 19: Analysis: controllability and similarity transformation
x (k + 1) = Ax (k) + Bu (k)
y (k) = Cx (k) + Du (k)
∗
d
P = B, AB, . . . , A
n−1
˜ ˜˜ ˜ ˜
B
▶ controllability matrix
= [T−1B, T−1AB, . . . , T−1An−1B] = T−1Pd
hence (A, B) controllable ⇔ (T−1AT, T−1B) controllable
▶ The controllability property is invariant under any coordinate transformation.
Controllability and Observability
y (k) = CTx∗ (k) + Du (k)
∗ −1 ∗ −1
x (k + 1) = T AT x (k) + T B u (k)
]
[

## Slide 20: * Popov-Belevitch-Hautus (PBH) controllability test
▶ the full rank condition of the controllability matrix
d
2 n−1
P = B, AB, A B, . . . , A B
[ ]
is equivalent to: the matrix [A − λI , B] having full row rank at every eigenvalue, λ, of A
▶ to see this: if [A − λI , B] is not full row rank then there exists nonzero vector (a left eigenvector) such that
v T [A − λI B] = 0
⇔ v T A = λv T
v T B = 0
i.e., the input vector B is orthogonal to a left eigenvector of A.
Controllability and Observability

## Slide 21: Example
Controllability and Observability
not full row rank
⇒uncontrollable
Intuition: x˙1 = λ1x1 is not impacted by the control input at all.

## Slide 22
Concepts
DT controllability
Controllability and controllable canonical form Controllability and Lyapunov Eq.
DT observability
Observability and observable canonical form
CT cases
The degrees of controllability and observability
Transforming controllable systems into controllable canonical forms
Transforming observable systems into observable canonical forms
Controllability and Observability

## Slide 23: Observability of LTI systems
Definition
A discrete-time linear system
x (k + 1) = A (k) x (k) + B (k) u (k)
y (k) = C (k) x (k) + D (k) u (k)
is called observable at k = 0 if ∃ a finite time k1 such that ∀ initial state x (0), the knowledge of {u (k) ; k = 0, 1, . . . , k1} and
{y (k) ; k = 0, 1, . . . , k1} suffice to determine the state x (0).
Otherwise, the system is said to be unobservable at time k = 0.
Controllability and Observability

## Slide 24: Observability of LTI systems
let us start with the unforced system
x (k + 1) = Ax (k) , A ∈ Rn
y (k) = Cx (k) , y ∈ Rm
x (k) = Akx (0) and y (k) = Cx (k) give
if the linear matrix equation has a nonzero solution x (0), the system is observable.
Controllability and Observability

## Slide 25: Observability of LTI systems
generalizing to
x (k + 1) = Ax (k) + Bu (k) , y (k) = Cx (k) + Du (k):
Controllability and Observability

## Slide 26: Observability of LTI systems
▶ x (0) can be solved if Qd has rank n (full column rank):
▶ if Qd is square, x (0) = Q−1Y
d
▶ if Qd is a tall matrix, pick n linearly independent rows from Qd
Controllability and Observability

## Slide 27: Observability of LTI systems Cont’d
▶ also, no need to go beyond n in Qd : adding CAn, CAn+1, . . . does not increase the column rank of Qd (Cayley Halmilton Theorem)
Controllability and Observability

## Slide 28: Theorem (Observability Theorem)
System x (k + 1) = Ax (k) + Bu (k) , y (k) = Cx (k) + Du (k), A ∈ Rn×n, C ∈ Rm×n is observable if and only if either one of the following is satisfied
1. The observability matrix
has full column rank
2. The observability gramian
is nonsingular for some finite k1
3. * PBF test: The matrix
has full column rank at
every eigenvalue, λ, of A.
Controllability and Observability

## Slide 29: Proof: from observability matrix to gramian
▶ Q
Controllability and Observability
d
is full column rank ⇒
is nonsingular

## Slide 30: Observability check
▶ analogous to the case in controllability, the observability property is invariant under any coordinate transformation:
(A, C ) is observable (T−1AT, CT ) is observable
▶ if A is Schur, k1 can be set to ∞ in the observability gramian
and we can compute by solving the Lyapunov equation
AT Wod A − Wod = −CT C
▶ the solution is nonsingular iff the system is observable
▶ in fact, Wod ⪰ 0 by definition ⇒ “nonsingular” can be replaced with “positive definite”
Controllability and Observability

## Slide 31: Observability and observable canonical form
▶ observability matrix
has full column rank
▶ system in observable canonical form is observable
Controllability and Observability

## Slide 32: * PBH test for observability
The matrix
has full column rank at every eigenvalue, λ, of A.
▶ if not full rank then there exists a nonzero eigenvector v :
Av = λv Cv = 0
⇒ CAv = λCv = 0
.
.
CAn−1v = 0
⇒
▶ the reverse direction is analogous
▶ interpretation: some non-zero initial condition x0 = v will generate zero output, which is not distinguishable from the origin.
Controllability and Observability
⇒ unobservable

## Slide 33
Concepts
DT controllability
Controllability and controllable canonical form Controllability and Lyapunov Eq.
DT observability
Observability and observable canonical form
CT cases
The degrees of controllability and observability
Transforming controllable systems into controllable canonical forms
Transforming observable systems into observable canonical forms
Controllability and Observability

## Slide 34: Theorem (Controllability of continuous-time systems)
The n-dimensional r -input LTI system with = Ax + Bu, A ∈ Rn×n, B ∈ Rn×r is controllable if and only if either one of the following is satisfied
The n × nr controllability matrix
P = [B, AB, A2B, . . . , An−1B]
has rank n.
The controllability gramian
is nonsingular for any t > 0.
Controllability and Observability

## Slide 35: Theorem (Observability of continuous-time systems)
System = Ax + Bu, y = Cx + Du, A ∈ Rn×n, C ∈ Rm×n is observable if and only if either one of the following is satisfied
1. The (mn) × n observability matrix
Controllability and Observability
has rank n (full column rank)
2. The observability gramian
is nonsingular for any t > 0

## Slide 36: Summary: computing the gramians
 | Controllability Gramian | Observability Gramian
continuous time |  | 
Lyapunov eq. if t → ∞ & A is Hurwitz stable | AWc + Wc AT = −BBT | AT Wo + Wo A = −CT C
discrete time |  | 
Lyapunov eq. if k1 → ∞ & A is Schur stable | AWcd AT − Wcd = −BBT | AT Wod A − Wod = −CT C
▶
( ) (
T
duality: (A, B) is controllable if and only if A, C = A , B
T
)
is observable
▶ prove by comparing the gramians
Controllability and Observability

## Slide 37: Exercise
▶ exercise: show that the system is not observable.
▶ in fact, by similarity transform = x , we get
where the third state is not observable.
Controllability and Observability

## Slide 38
Concepts
DT controllability
Controllability and controllable canonical form Controllability and Lyapunov Eq.
DT observability
Observability and observable canonical form
CT cases
The degrees of controllability and observability
Transforming controllable systems into controllable canonical forms
Transforming observable systems into observable canonical forms
Controllability and Observability

## Slide 39: The degree of controllability
consider two systems
▶ both systems are controllable:
▶ however, Pd2 is nearly singular ⇒ S2 not “easy” to control
▶ e.g., to move from x (0) = [0, 0]T to [1, 1]T in two steps:
x (2) = Ax (1) + Bu (1) = A2x (0) + ABu (0) + Bu (1)
d
P [u (1) u (0)]T = x (2) − A2x (0)
Controllability and Observability

## Slide 40: The degree of controllability
▶ e.g., to move from x (0) = [0, 0]T to [1, 1]T in two steps:
x (2) = Ax (1) + Bu (1) = A2x (0) + ABu (0) + Bu (1)
S2 : {u (0) , u (1)} = {100, −99}
▶ needed control sequence
S1 : {u (0) , u (1)} = {1, 1}
⇒ more energy for S2!
Controllability and Observability
d
P [u (1) u (0)]T = x (2) − A2x (0)

## Slide 41: The degree of controllability: multi-input case
consider two systems
▶ both systems are controllable:
▶ degree of controllability reflected in the controllability Gramian:
Wcd 2 is almost singular (eigenvalues at 0.0001 and 3.0001)
Controllability and Observability

## Slide 42: The degree of controllability: multi-input case
▶ for general stable and controllable systems Σ = (A, B, C, D),
Wcd is computed from the Lyapunov Equation
AWcd AT − Wcd = −BBT
▶ if Wcd have eigenvalues close to zero, then the system is more difficult to control in the sense that it requires more energy in the input to steer the states in the state space
Controllability and Observability

## Slide 43: The degree of observability
consider two systems
▶ both systems are observable:
▶ however, Qd2 is nearly singular, hinting that S2 is not “easy” to observe
▶ e.g., to infer x (0) = [2, 1]T , the two measurements y (0) = 2 and
y (1) = CAx (0) = 2.001 are nearly identical in S2!
Controllability and Observability

## Slide 44: The degree of observability: multi-output case
▶ for general stable and controllable systems Σ = (A, B, C, D), the observability matrix Qd is not square
▶ the degree of observability is reflected in the eigenvalues of the observability Gramian Wod
▶ for stable systems, Wod is computed from the Lyapunov Equation AT Wod A − Wod = −CT C
▶ if Wod have eigenvalues close to zero, then the system is more difficult to observe
Controllability and Observability

## Slide 45: Balanced state-space realizations
we know now
▶ the controllability and observability Gramians represent the degrees of controllability and observability
▶ easily controllable systems may not be easily observable
▶ easily observable systems may not be easily controllable
⇒ there exists realizations that balance the two degrees of controllability and observability
Controllability and Observability

## Slide 46: Balanced state-space realizations
consider a stable system Σ = (A, B, C, D) in a minimal1 realization
▶ minimal realization ⇒ Σ is controllable and observable
▶ stable ⇒ can compute the Gramians from Lyapunov Equations
▶ if Wcd and Wod are equal and diagonal, then Σ is called a balanced realization
▶ i.e., there exists a diagonal matrix M = diag (σ1, σ2, . . . , σn), σ1 ≥ σ2 ≥ · · · ≥ σn > 0 such that
M = AMAT + BBT
M = AT MA + CT C
1i.e., dim A is the minimal order of the system
Controllability and Observability

## Slide 47
Concepts
DT controllability
Controllability and controllable canonical form Controllability and Lyapunov Eq.
DT observability
Observability and observable canonical form
CT cases
The degrees of controllability and observability
Transforming controllable systems into controllable canonical forms
Transforming observable systems into observable canonical forms
Controllability and Observability

## Slide 48: Transforming single-input controllable system into ccf
If system is controllable, we show how to transform the state equation into the controllable canonical form.
▶ goal 1: B˜ be in controllable canonical form ⇔
Controllability and Observability
m , then
Let x = Mx˜, where M = m
1
n
| | | |
m2 . . .
| | | |

## Slide 49: Transforming SI controllable system into ccf
Let x = Mx˜, where M = [m1, m2, . . . , mn], then
▶ goal 2: A˜ be in controllable canonical form⇔
A [m1, m2, . . . , mn] =
[m1, m2, . . . , mn]
.
.
. .
.
.
. .
0 1 0 . . . 0
. 0 0
. . . . . 1
0 . . . 0 0
−a0 −a1 . . . . . .
. 0
1
−an−1
Controllability and Observability

## Slide 50: Transforming SI controllable system into ccf
Let x = Mx˜, where M = [m1, m2, . . . , mn], then
▶ solving goals 1 and 2 yields
mn = B
mn−1 = Amn + an−1mn
mn−2 = Amn−1 + an−2mn
mi−1 = Ami + ai−1mn, i = n, . . . , 2
▶ when implementing, obtain a0, a1, . . . , an−1 first by calculating
det (sI − A) = sn + an−1sn−1 + · · · + a1s + a0
Controllability and Observability

## Slide 51: Transforming single-output (SO) observable system into ocf
−1 T T T
1 2 n
[ ]
T
Let x = R x˜, where R = r , r , . . . , r (
i
r is a row vector).
If system is observable, we show how to transform the state equation into the observable canonical form.
▶ goal 1: C˜ be in observable canonical form ⇔
Controllability and Observability

## Slide 52: Transforming SO observable system into ocf
▶ goal 2: A˜ be in observable canonical form⇔
Controllability and Observability
A =
−a
n−1
.
. .
.
. 0
0
. . . . . .
−a
1
.
. .
. . .
. .
. 0
1
−a0 0 . . . 0 0
1 0 . . . 0
. . . .
−1 T T T
1 2 n
[ ]
T
Let x = R x˜, where R = r , r , . . . , r (
i
r is a row vector).

## Slide 53: Transforming SO observable system into ocf
▶ solving goals 1 and 2 yields
r1 = C
r2 = r1A + an−1r1
r3 = r2A + an−2r1
ri +1 = ri A + an−ir1, i = 1, . . . , n − 1
▶ obtain a0, a1, . . . , an−1 first by calculating det (sI − A)
Controllability and Observability
−1 T T T
1 2 n
[ ]
T
Let x = R x˜, where R = r , r , . . . , r (
i
r is a row vector).

## Slide 54: Transforming SO observable system into ocf
Example
x (k + 1) =
1 0.01
0 0
x (k)
det (A − λI )=λ2 − λ ⇒ a1 = −1, a0 = 0
r1 = C = [1, 0]
r2 = r1C + a1r1 = [1, 0]A + (−1) [1, 0]
R =
1 0
0 0.01
−1
, R =
1 0
0 100
C˜ = CR−1 = [1, 0] ⇐ ocf!
˜
−1
A = RAR =
1 1
0 0
⇐ ocf!
Controllability and Observability
y (k) = [ 1 0 ] x (k)