## Slide 1: State Feedback Control
Linear Systems

## Slide 2: Motivation
▶ At the center of designing control systems is the idea of feedback.
▶ In such transfer-function approaches as lead-lag and root locus methods, the primal goal is to achieve a proper map of
closed-loop poles with output feedback.
Key questions:
▶ How much freedom do we have for state-space systems?
▶ Are there fundamental system properties that yield higher achievable performance?
▶ How to implement the design algorithms?
State Feedback

## Slide 3: 1. Goal and realization of state feedback
2. Closed-loop eigenvalue placement by state feedback
State Feedback

## Slide 4: Goal
Consider an n-dimensional state-space system
Σ :
(t) = Ax (t) + Bu(t)
y (t) = Cx (t) + Du(t)
x (t0) = x0
where x ∈ Rn, u ∈ Rr , and y ∈ Rm.
▶ Denominators of the transfer function
G (s) = C (sI − A)−1 B + D come from the characteristic polynomial det (sI − A) that arises when computing the inverse (sI − A)−1.
▶ We shall investigate the use of feedback to alter the qualitative behavior of the system by changing the eigenvalues of the closed-loop “A” matrix.
State Feedback

## Slide 5: Realization
= Ax + Bu, y = Cx + Du
K
Consider the state-feedback law
u = −Kx + v
▶ v : new input which we will deal with later
▶ K ∈ Rm×n: n-number of states, m-number of inputs
▶ closed-loop system:
(1)
cl
Σ :
(t) = (A − BK ) x (t) + Bv (t)
y (t) = Cx (t) + Du(t)
x (t0) = x0 (2)
▶ key closed-loop property: eigenvalues of A − BK .
▶ How freely can we place the eigenvalues of Acl = A − BK ?
State Feedback
v
y
u
x
+
-

## Slide 6: 1. Goal and realization of state feedback
2. Closed-loop eigenvalue placement by state feedback
State Feedback

## Slide 7: Eigenvalue placement by state feedback
Fact
If Σ = (A, B, C, D) is in controllable canonical form, we can completely change all the eigenvalues of A − BK by choice of state-feedback gain matrix K.
▶ Problem setup: single-input single-output system in c.c.f.
(3)
State Feedback

## Slide 8: Eigenvalue placement by state feedback: c.c.f.
▶ | Goal: achieve desired closed-loop eigenvalue locations p1, , pn, i.e. | 
 | det (sI − (A − BK )) = (s − p1)(s − p2) (s − pn) | (4)
 | = sn + γn−1sn−1 + + γ1s + γ0 | (5)
▶ | Let K = [k0, k1, . . . , kn−1]. The structured A and B give | 
▶ |  | 
 |  | (4)
 |  | (5)
▶ | Let K = [k0, k1, . . . , kn−1]. The structured A and B give | 
State Feedback

## Slide 9: Eigenvalue placement by state feedback: c.c.f.
▶ A and A − BK have the same structure
▶ the only difference is the last row:
matrix last row
A
A − BK
▶ recall (3): det (sI − A) = sn + αn−1sn−1 + + α1s + α0.
▶ thus
▶ hence
k0 = γ0 − α0
kn−1 = γn−1 − αn−1
State Feedback

## Slide 10: Eigenvalue placement by state feedback: c.c.f.
Eigenvalue-placement Algorithm
determine desired eigenvalue locations p1, · · · , pn
calculate desired closed-loop characteristic polynomial
(s − p1)(s − p2) (s − pn) = sn + γn−1sn−1 + + γ1s + γ0
calculate open-loop characteristic polynomial
det(sI − A) = sn + αn−1sn−1 + + α1s + α0
define the matrices:
K = [γ0 − α0, . . . , γn−1 − αn−1]
Powerful result: if the system is in controllable canonical form, we can arbitrarily place the closed-loop eigenvalues by state feedback!
State Feedback

## Slide 11: General eigenvalue placement by state feedback
▶ What if the given state-space realization Σ = (A, B, C, D) is not in the required form?
▶ We can then transform it to c.c.f. via a similarity transformation (See lecture on controllability and observability).
▶ Powerful fact: if system Σ = (A, B, C, D) is controllable, then we can arbitrarily place the closed-loop eigenvalues via state feedback.
State Feedback

## Slide 12: Stabilization
▶ if a single-input system is uncontrollable, arbitrary closed-loop eigenvalue plaement is not available
▶ Kalman decomposition gives
applying controll law
gives
State Feedback

## Slide 13: Stabilization cont’d
▶ closed-loop dynamics
▶ closed-loop eigenvalues come from
▶ ⇒: single-input systems are stabilizable if and only if the uncontrollable portion of the system does not have any unstable eigenvalue.
State Feedback

## Slide 14: Discrete-time case
▶ the eigenvalue assignment of discrete-time systems is analogous:
▶ system dynamics:
x (k + 1) = Ax (k) + Bu (k)
y (k) = Cx (k)
▶ controller: u (k) = −Kx (k) + v (k)
▶ closed-loop dynamics:
x (k + 1) = Ax (k)−BKx (k)+Bv (k) = (A − BK ) x (k)+Bv (k)
▶ arbitrary closed-loop eigenvalue assignment if system is controllable
State Feedback

## Slide 15: The case with output feedback
= Ax + Bu
= Cx
= −Fy + v
▶ if the full state is not measurable, state feedback control is not feasible
▶ consider output feedback
y
u
⇒ = Ax − BFy + Bv = (A − BFC ) x + Bv
▶ A − BFC not as structured as A − BK (exercise: write out the case for SISO systems)
▶ arbitrary closed-loop eigenvalue assignment not feasible
State Feedback

## Slide 16: The case with output feedback
Example
Controllable mass-spring-damper system
▶ arbitrary closed-loop eigenvalue assignment if u∗ = −k1x1 −k2x2, namely U∗(s) = −k1X1(s) − k2X2(s) = − (k1 + k2s) X1(s) ⇒ a proportional plus derivative (PD) control law
▶ if with only proportional control, u∗ = −k1x1, arbitrary closed-loop eigenvalue assignment is not possible
State Feedback