## Slide 1: Introduction to Modern Controls Relationship Between State-Space Models and Transfer Functions
From State Space to Transfer Functions

## Slide 2: Continuous-time LTI state-space description
dt
d x(t) = Ax(t) + Bu(t)
y(t) = Cx(t) + Du(t)
From State Space to Transfer Functions
u (t)
System
x1,x2,...,xn
y(t)

## Slide 3: Recap: LTI input/output description
From State Space to Transfer Functions
u (t)
System
x1,x2,...,xn
y(t)
let u (t) ∈ R and y (t) ∈ R, then
where g (t) is the system’s impulse response Laplace domain:
Y(s) = G(s)U(s)

## Slide 4: From state space to transfer function
From State Space to Transfer Functions
given , , , ,
when , we have
–the transfer function between and

## Slide 5: Analogously for discrete-time systems
From State Space to Transfer Functions
5 / 14
for , , , ,
when , we have
–the transfer function between and

## Slide 6: From state space to transfer function: Observations
From State Space to Transfer Functions
dimensions:
uniqueness: is unique given the state-space model

## Slide 7: Matrix inverse
From State Space to Transfer Functions
where
e.g.: ,
where , , , , , , , ,

## Slide 8: Mass-spring-damper
position: y(t)
m
k
b
u = F
From State Space to Transfer Functions

## Slide 9: Mass-spring-damper
From State Space to Transfer Functions

## Slide 10: Mass-spring-damper
From State Space to Transfer Functions

## Slide 11: Mass-spring-damper
From State Space to Transfer Functions
Putting the inverse in yields
namely

## Slide 12: Numerical example in MATLAB
position: y(t)
m
k
b
u = F
m = 1; k = 2; b = 1;
A = [0 1; -k/m -b/m];
B = [0; 1/m];
C = [1 0];
D = 0;
sys = ss(A,B,C,D)
[num,den] = ss2tf(A,B,C,D); sys_tf = tf(num,den) figure, step(sys)
figure, step(sys_tf)
From State Space to Transfer Functions

## Slide 13: Numerical example in Python
import control as co import numpy as np
m = 1
k = 2
b = 1
A = np.array([[0,1],[-k/m,-b/m]])
B = np.array([[0], [1/m]])
C = np.array([1,0])
D = np.array([0])
sys = co.ss(A,B,C,D) print(sys)
sys_tf = co.ss2tf(sys) print(sys_tf)
print(co.poles(sys)) print(co.poles(sys_tf))
From State Space to Transfer Functions

## Slide 14: Exercise
From State Space to Transfer Functions
Given the following state-space system parameters: , , , , obtain the transfer function .