## Slide 1: Linear Systems: Stability
Stability

## Slide 2
Definitions in Lyapunov stability analysis
Stability of LTI systems: method of eigenvalue/pole locations
Lyapunov’s approach to stability Relevant tools
Lyapunov stability theorems Instability theorem
Discrete-time case
Recap
Stability

## Slide 3: Finite dimensional vector norms
Stability
3 / 83
Let v ∈ Rn. A norm is:
▶ a metric in vector space: a function that assigns a real-valued
length to each vector in a vector space
▶
e.g., 2 (Euclidean) norm:
default in this set of notes:

## Slide 4: Equilibrium state
Stability
4 / 83
For an n-th order unforced system
= f (x, t) , x (t0) = x0
an equilibrium state/point xe is one such that
f (xe, t) = 0, ∀t
▶ the condition must be satisfied by all t ≥ 0
▶ if a system starts at equilibrium state, it stays there

## Slide 5: Equilibrium state of a linear system
For a linear system
(t) = A(t)x (t), x (t0) = x0
▶ origin xe = 0 is always an equilibrium state
▶ when A(t) is singular, multiple equilibrium states exist
Stability
5 / 83

## Slide 6: Lyapunov’s definition of stability
▶ The equilibrium state 0 of = f (x, t) is stable in the sense of Lyapunov (s.i.L) if for all ϵ > 0, and t0, there exists δ (ϵ, t0) > 0 such that ∥x (t0) ∥2 < δ gives ∥x (t) ∥2 < ϵ for all t ≥ t0
Figure: Stable s.i.L: ∥x (t0) ∥ < δ ⇒ ∥x (t) ∥ < ϵ ∀t ≥ t0.
Stability
6 / 83

## Slide 7: Asymptotic stability
The equilibrium state 0 of = f (x, t) is asymptotically stable if
▶ it is stable in the sense of Lyapunov, and
▶ for all ϵ > 0 and t0, there exists δ (ϵ, t0) > 0 such that
∥x (t0) ∥2 < δ gives x (t) → 0
Figure: Asymptotically stable i.s.L: ∥x (t0) ∥ < δ ⇒ ∥x (t) ∥ → 0.
Stability
7 / 83

## Slide 8
Definitions in Lyapunov stability analysis
Stability of LTI systems: method of eigenvalue/pole locations
Lyapunov’s approach to stability Relevant tools
Lyapunov stability theorems Instability theorem
Discrete-time case
Recap
Stability

## Slide 9: Stability of LTI systems: method of eigenvalue/pole locations
Stability
9 / 83
the stability of the equilibrium point 0 for = Ax or
x (k + 1) = Ax (k) can be concluded immediately based on λ (A):
▶ the response eAtx (t0) involves modes such as eλt , teλt , eσt cos ωt, eσt sin ωt
▶ the response Akx (k0) involves modes such as λk , kλk−1, r k cos kθ, r k sin kθ
▶ eσt → 0 if σ < 0; eλt → 0 if λ < 0
▶ λk → 0 if |λ| < 1; r k → 0 if |r | = || = |λ| < 1

## Slide 10
Stability of the origin for x˙ = Ax
stability λi (A) at 0
unstable Re {λi } > 0 for some λi or Re {λi } ≤ 0 for all λi ’s but for a repeated λm on the imaginary axis with multiplicity m, nullity (A − λmI ) < m (Jordan form)
stable Re {λi } ≤ 0 for all λi ’s and ∀ repeated λm on the i.s.L imaginary axis with multiplicity m, nullity (A − λmI ) = m (diagonal form)
asymptotically Re {λi } < 0 ∀λi (A is then called Hurwitz stable) stable
Stability

## Slide 11
Stability
11 / 83
Example (Unstable moving mass)
▶ λ1 = λ2 = 0, m = 2,
i
nullity (A − λ I ) = nullity
= 1 < m
▶ i.e., two repeated eigenvalues but needs a generalized
eigenvector ⇒ Jordan form after similarity transform
▶
At
verify by checking e =
: t grows unbounded

## Slide 12: Example (Stable in the sense of Lyapunov)
Stability
12 / 83
▶ λ1 = λ2 = 0, m = 2,
▶
At
verify by checking e =
i
nullity (A − λ I ) = nullity
= 2 = m

## Slide 13: Routh-Hurwitz criterion
▶ the Routh Test (by E.J. Routh, in 1877): a simple algebraic procedure to determine how many roots a given polynomial
A(s) = ansn + an−1sn−1 + · · · + a1s + a0
has in the closed right-half complex plane, without the need to explicitly solve for the roots
▶ German mathematician Adolf Hurwitz independently proposed in 1895 to approach the problem from a matrix perspective
▶ popular if stability is the only concern and no details on eigenvalues (e.g., speed of response) are needed
Stability
13 / 83

## Slide 14: Routh-Hurwitz criterion
▶ the asymptotic stability of the equilibrium point 0 for = Ax
can also be concluded based on the Routh-Hurwitz criterion
▶ simply apply the Routh Test to A(s) = det (sI − A)
▶ recap: the poles of transfer function G (s) = C (sI − A)−1 B + D
come from det (sI − A) in computing the inverse (sI − A)−1
Stability
14 / 83

## Slide 15: The Routh Array
for A(s) = ansn + an−1sn−1 + · · · + a1s + a0, construct
an−2 an−4 an−6
· · ·
· · ·
an
an−1 an−3 qn−2 qn−4
an−5 an−7 qn−6
· · ·
sn sn−1 sn−2 sn−3
qn−3
qn−5
qn−7
· · ·
.
.
.
.
.
.
s1
s0
. .
x2 x0
x0
▶ first two rows contain the coefficients of A(s)
▶ third row constructed from the previous two rows via
b d
x ·
y ·
a
c
·
bc − ad
·
· · ·
·
Stability
15 / 83
c
xc − ay
c
·

## Slide 16: The Routh Array
for A(s) = ansn + an−1sn−1 + · · · + a1s + a0, construct
· · ·
an−6 an−7
· · ·
an an−2
an−1 an−3 qn−2 qn−4
an−4 an−5 qn−6
· · ·
sn sn−1 sn−2 sn−3
qn−3
qn−5
qn−7
· · ·
.
.
.
.
.
.
s1
s0
. .
x2 x0
x0
▶ All roots of A(s) are on the left half s-plane if and only if all elements of the first column of the Routh array are positive.
Stability
16 / 83

## Slide 17: The Routh Array
Stability
17 / 83
Example (A(s) = 2s4 + s3 + 3s2 + 5s + 10)
2 | 3 | 10
1 | 5 | 0
2×5
3 − = −7
s4 s3 s2 s1
5 −
1 1×10
−7
0
s 10
10 | 0
0 | 0
0 | 0
▶ two sign changes in the first column
▶ unstable and two roots in the right half side of s-plane

## Slide 18: The Routh Array
special cases:
▶ If the 1st element in any one row of Routh’s array is zero, one can replace the zero with a small number ϵ and proceed further.
▶ There are other possible complications, which we will not pursue further. See, e.g. "Automatic Control Systems", by Kuo, 7th ed., pp. 339-340.
Stability
18 / 83

## Slide 19: Stability of the origin for x (k + 1) = f (x (k), k)
▶ stability analysis follows analogously for nonlinear time-varying discrete-time systems of the form
x (k + 1) = f (x (k), k) , x (k0) = x0
▶ equilibrium point xe :
f (xe, k) = xe, ∀k
▶ without loss of generality, 0 is assumed an equilibrium point
Stability
19 / 83

## Slide 20
Stability of the origin for x (k + 1) = Ax (k)
stability λi (A) at 0
unstable ¦λi ¦ > 1 for some λi or ¦λi ¦ ≤ 1 for all λi ’s but for a repeated λm on the unit circle with multiplicity m, nullity (A − λmI ) < m (Jordan form)
stable ¦λi ¦ ≤ 1 for all λi ’s but for any repeated λm on the unit i.s.L circle with multiplicity m, nullity (A − λmI ) = m (diagonal form)
asymptotically ¦λi ¦ < 1 ∀λi (such a matrix is called Schur stable) stable
Stability

## Slide 21: Routh-Hurwitz criterion for DT LTI systems
▶ the stability domain |λi | < 1 is a unit disk
▶ Routh array validates stability in the left-half plane
▶ bilinear transformation maps the closed left half s-plane to the closed unit disk in z -plane
Real
Real
Imaginary Imaginary
s-plane z -plane
1
1−s
z = 1+s or s = z−1
z +1
−1
Stability
21 / 83

## Slide 22: Routh-Hurwitz criterion for DT LTI systems
Stability
▶ Given A(z ) = zn + a1zn−1 + · · · + an, procedures of Routh-Hurwitz test:
▶ apply bilinear transform
▶ apply Routh test to

## Slide 23: Routh-Hurwitz criterion for DT LTI systems
Stability
23 / 83
Example (A(z ) = z 3 + 0.8z 2 + 0.6z + 0.5)
z = 1−s
3
3 2
▶ A∗(s) = A(z )| 1+s (1 − s) = (1 + s) + 0.8 (1 + s) (1 − s) +
0.6 (1 + s) (1 − s)2 + 0.5 (1 − s)3 = 0.3s3 + 3.1s2 + 1.7s + 2.9
▶ Routh array
s3 s2
s 1.7 −
s0
0.3
3.1
0.3×2.9
3.1
2.9
1.7
2.9
= 1.42 0
0
▶ all elements in first column are positive ⇒ roots of A(z ) are all in the unit circle

## Slide 24
Definitions in Lyapunov stability analysis
Stability of LTI systems: method of eigenvalue/pole locations
3. Lyapunov’s approach to stability Relevant tools
Lyapunov stability theorems Instability theorem
Discrete-time case
4. Recap
Stability

## Slide 25: Stability of LTI systems: method of eigenvalue/pole locations
▶ λk → 0 if |λ| < 1; r k → 0 if |r | = = |λ| < 1
the stability of the equilibrium point 0 for = Ax or
x (k + 1) = Ax (k) can be concluded immediately based on λ (A):
▶ the response eAtx (0) involves modes such as eλt , teλt , eσt cos ωt, eσt sin ωt
▶ the response Akx (0) involves modes such as λk , kλk−1, r k cos kθ, r k sin kθ
▶ eσt → 0 if σ < 0; eλt → 0 if λ < 0
Stability
25 / 83

## Slide 26: Lyapunov’s approach to stability
The direct method of Lyapunov to stability problems:
▶ no need for explicit solutions to system responses
▶ an “energy” perspective
▶ fit for general dynamic systems (linear/nonlinear, time-invariant/time-varying)
Stability
26 / 83

## Slide 27: Stability from an energy viewpoint: Example
Consider spring-mass-damper systems:
▶ λ (A)’s are in the left-half s-plane⇒ asymptotically stable
▶ total energy
▶ energy dissipates / is dissipative:
▶ = 0 only when x2 = 0. As [x1, x2]T = 0 is the only equilibrium, the motion will not stop at x2 = 0, x1 ≠ 0. Thus energy will keep decreasing toward 0 which is achieved at the origin.
Stability
(x1: position; x2 : velocity)
(Newton’s law)
(t) = potential energy + kinetic energy =

## Slide 28: Stability from an energy viewpoint: Generalization
Consider unforced, time-varying, nonlinear systems
(t) = f (x (t), t) , x (t0) = x0
x (k + 1) = f (x (k), k) , x (k0) = x0
▶ assume the origin is an equilibrium state
▶ energy function ⇒ Lyapunov function: a scalar function of x
and t (or x and k)
▶ goal is to relate properties of the state through the Lyapunov function
▶ main tool: matrix formulation, linear algebra, positive definite functions
Stability
28 / 83

## Slide 29: Relevant tools
Quadratic functions
▶ intrinsic in energy-like analysis, e.g.
▶ convenience of matrix formulation:
▶ general quadratic functions in matrix form
Q (x ) = x T Px, PT = P
Stability
29 / 83

## Slide 30: Relevant tools
Symmetric matrices
▶ recall: a real square matrix A is
▶ symmetric if A = AT
▶ skew-symmetric if A = −AT
▶ examples:
▶ Any real square matrix can be decomposed as the sum of a
symmetric matrix and a skew-symmetric matrix:
general case: P =
+
P + PT P − PT
2 2
Stability
30 / 83
e.g.

## Slide 31: Relevant tools
Symmetric matrices
▶ a real square matrix A ∈ Rn×n is orthogonal if AT A = AAT = I
▶ meaning that the columns of A form a orthonormal basis of Rn
Stability
31 / 83
namely, and .

## Slide 32: Theorem
T
Also, u u
∈ R. Thus λ =
T
u Au
uT u
must also be a real number.
Stability
32 / 83
= uT
= uT A
= uT AT
= λuT
= λ T u
= T Au
The eigenvalues of symmetric matrices are all real.
Proof: ∀ : A ∈ Rn×n with AT = A.
Eigenvalue-eigenvector pair: Au = λu ⇒ T Au = λ T u, where is the complex conjugate of u. T Au is a real number, as
∵ A ∈ Rn×n
∵ A = AT
∵ (Au)T = (λu)T
∵ uT ∈ R
∵ Au = λu

## Slide 33
Example
▶
▶
Stability
33 / 83
:
:
import numpy as np #larger-scale Python example N = 100
P = np.random.randint(-200,200,size=(N,N))
P_symm = (P + P.T)/2
lambdas, _ = np.linalg.eig(P_symm) print(lambdas)

## Slide 34: Theorem
The eigenvalues of skew-symmetric matrices are all imaginary or zero.
▶
Stability
34 / 83
:
import numpy as np N = 100
P = np.random.randint(-200,200,size=(N,N))
P_symm = (P - P.T)/2
lambdas, _ = np.linalg.eig(P_symm) print(lambdas)

## Slide 35: Theorem
All eigenvalues of an orthogonal matrix have a magnitude of 1.
▶
Stability
35 / 83
import numpy as np
from scipy.linalg import qr n = 3
H = np.random.randn(n, n) Q, _ = qr(H)
print (np.dot(Q,Q.T))
print (np.dot(Q.T,Q))
:

## Slide 36: Important properties of symmetric matrices
Theorem
The eigenvalues of symmetric matrices are all real.
Theorem
The eigenvalues of skew-symmetric matrices are all imaginary or zero.
Theorem
All eigenvalues of an orthogonal matrix have a magnitude of 1.
matrix structure analogy in complex plane
symmetric skew-symmetric
orthogonal
real line imaginary line unit circle
Stability
36 / 83

## Slide 37: The spectral theorem for symmetric matrices
When A ∈ Rn×n has n distinct eigenvalues, we can do diagonalization
A = UΛU−1. When A is symmetric, things are even better:
Theorem (Symmetric eigenvalue decomposition (SED))
∀ : A ∈ Rn×n, AT = A, there always exist λi ∈ R and ui ∈ Rn, s.t.
n
i i
i
A = λ u u = UΛU
T T
(1)
i =1
▶ λi ’s: eigenvalues of A
▶ ui : eigenvector associated to λi , normalized to have unity norms
▶ U = [u1, u2, · · · , un] is orthogonal: UT U = UUT = I
▶ Λ = diagonal (λ1, λ2, . . . , λn)
Stability
37 / 83

## Slide 38: Elements of proof for SED
Theorem
∀ : A ∈ Rn×n with AT = A, then eigenvectors of A, associated with
different eigenvalues, are orthogonal.
Proof.
i i i
Let Aui = λiui and Auj = λjuj . Then uT Auj = uT λjuj = λjuT uj .
i i i
i i
Also, uT Auj = uT AT uj = (Aui )T uj = λiuT uj . So λiuT uj = λjuT uj .
i j
T
i
But λ ≠ λ . It must be that u u
j
= 0.
SED now follows:
▶ If A has distinct eigenvalues, then U = [u1, u2, · · · , un] is orthogonal after normalizing all the eigenvectors to unity norm.
▶ If A has r (< n) distinct eigenvalues, we can choose multiple orthogonal eigenvectors for the eigenvalues with none-unity multiplicities.
Stability
38 / 83

## Slide 39: Rethinking symmetric matrices
With the spectral theorem, next time we see a symmetric matrix A, we immediately know that
▶ λi is real for all i
▶ associated with λi , we can always find a real eigenvector
▶
i
n
i =1
∃ an orthonormal basis {u } , which consists of the
eigenvectors
▶ if A ∈ R2×2, then if you compute first λ1, λ2 and u1, you won’t
need to go through the regular math to get u2, but can simply solve for a u2 that is orthogonal to u1 with ∥u2∥ = 1.
Stability
39 / 83

## Slide 40
Example: A =
Computing the eigenvalues gives
det
⇒λ1 = 4, λ2 = 8
▶ first normalized eigenvector:
▶
choose t2 =
Stability
= 35 − 12λ + λ2 − 3 = (λ − 4) (λ − 8) = 0
(A − λ1I ) t1 = 0 ⇒
t1 = 0 ⇒ t1 =
A is symmetric ⇒ eigenvectors are orthogonal to each other:
. No need to solve (A − λ2I ) t2 = 0!

## Slide 41: Theorem (Eigenvalues of symmetric matrices)
Stability
If A = AT ∈ Rn×n, then the eigenvalues of A satisfy
(2)
(3)
Proof.
Perform SED to get where spans . Then any vector can be decomposed as . Thus

## Slide 42: Positive definite matrices
▶ eigenvalues of symmetric matrices are real ⇒ we can order the eigenvalues
▶ a symmetric matrix P is called positive-definite if all its eigenvalues are positive
▶ equivalently:
Definition (Positive Definite Matrices)
A symmetric matrix P ∈ Rn×n is called positive-definite, written
P ≻ 0, if x T Px > 0 for all x (≠0) ∈ Rn.
P is called positive-semidefinite, written P ⪰ 0, if x T Px ≥ 0 for all x ∈ Rn
▶ P ≻ 0 (P ⪰ 0) ⇔ P can be decomposed as P = NT N where N
is nonsingular (singular)
Stability
42 / 83

## Slide 43: Negative definite matrices
Definition
A symmetric matrix Q ∈ Rn×n is called negative-definite, written
Q ≺ 0, if −Q ≻ 0, i.e., x T Qx < 0 for all x (≠0) ∈ Rn.
Q is called negative-semidefinite, written Q ⪯ 0, if x T Qx ≤ 0 for all x ∈ Rn
Stability
43 / 83

## Slide 44
Updated matrix analogies
matrix structure | eigenvalues | analogy in complex plane
symmetric | real | real axis
skew-symmetric | on imaginary axis | imaginary axis
orthogonal | magnitude 1 | unit circle
positive definite | positive | R+ axis
negative definite | negative | R− axis
Stability

## Slide 45: Caution
▶ positive-definite matrices can have negative entries:
Example
Stability
45 / 83
is positive-definite, as P = P and take any
P =
T
v = [x, y ]T , we have
v T Pv =
= 2x 2 + 2y 2 − 2xy
= x 2 + y 2 + (x − y )2 ≥ 0
and the equality sign holds only when x = y = 0.

## Slide 46: Caution
▶ conversely, matrices whose entries are all positive are not necessarily positive-definite:
Example
A =
is not positive-definite:
Stability
46 / 83

## Slide 47: Positive definite matrices
Theorem
For a symmetric matrix P, P ≻ 0 if and only if all the eigenvalues of
P are positive.
Proof.
Since P is symmetric, we have
(4)
(5)
Stability
47 / 83
x T Ax > 0, x0 ⇔ λmin > 0.
which gives . Thus

## Slide 48: Relevant tools Checking positive definiteness of a matrix.
We often use the following necessary and sufficient conditions to check positive (semi-)definiteness:
▶ P ≻ 0 (P ⪰ 0) ⇔ the leading principle minors defined below are positive (nonnegative)
Definition
Stability
48 / 83
The leading principle minors of P =
are defined as
11
p , det
, det P.

## Slide 49: Relevant tools Checking positive definiteness of a matrix.
Example
None of the following matrices are positive definite:
Stability

## Slide 50
Recap
Stability
energy
quadratic function
symmetric matrix

## Slide 51
Recap
Stability
Lyapunov function
energy
quadratic function
symmetric matrix

## Slide 52: Recap
Stability
energy
quadratic function
symmetric matrix
positive definite function
positive definite matrix
for linear system
Lyapunov function

## Slide 53: Relevant tools
Definition (Positive Definite Functions)
A continuous time function W : Rn → R+, called to be PD, satisfying
▶ W (x ) > 0 for all x0
▶ W (0) = 0
▶ W (x ) → ∞ as |x | → ∞ uniformly in x
In the 3D space, positive definite functions are “bowl-shaped”, e.g.,
1 2
W (x1, x2) = x 2 + x 2 .
Stability
53 / 83

## Slide 54: Relevant tools
locally, e.g., W (x , x ) = x + sin x for x ∈ R and |x | < π
Definition (Locally Positive Definite Functions)
A continuous time function W : Rn → R+, called to be LPD, satisfying
▶ W (x ) > 0 for all x0 and |x | < r
▶ W (0) = 0
In the 3D space, locally positive definite functions are “bowl-shaped”
1 2
1
2 2
2 1 2
Stability
54 / 83

## Slide 55: Relevant tools
Exercise
Let x = [x1, x2, x3]T . Check the positive definiteness of the following functions
1 2 3
1. V (x ) = x 4 + x 2 + x 4 (PD)
2
1
2
3
2 2 4
3
3
2. V (x ) = x + x + 3x − x (LPD for |x | <)
Stability
55 / 83

## Slide 56
Definitions in Lyapunov stability analysis
Stability of LTI systems: method of eigenvalue/pole locations
3. Lyapunov’s approach to stability Relevant tools
Lyapunov stability theorems Instability theorem
Discrete-time case
4. Recap
Stability

## Slide 57: Lyapunov stability theorems
▶ recall the spring mass damper example in matrix form
▶ energy function is PD:
Stability
57 / 83
and its derivative is NSD:
(6)
(7)
(t) = potential energy + kinetic energy =

## Slide 58: Theorem
The equilibrium point 0 of (t) = f (x (t), t) , x (t0) = x0 is stable in the sense of Lyapunov if there exists a locally positive definite function V (x, t) such that (x, t) ≤ 0 for all t ≥ t0 and all x in a local region x : |x | < r for some r > 0.
▶ such a V (x, t) is called a Lyapunov function
▶ i.e., V (x ) is PD and (x ) is negative semidefinite in a local region |x | < r
Theorem
The equilibrium point 0 of (t) = f (x (t), t) , x (t0) = x0 is locally asymptotically stable if there exists a Lyapunov function V (x ) such that (x ) is locally negative definite.
Stability
58 / 83

## Slide 59
Theorem
The equilibrium point 0 of (t) = f (x (t), t) , x (t0) = x0 is globally asymptotically stable if there exists a Lyapunov function V (x ) such that V (x ) is positive definite and (x ) is negative definite.
Stability
59 / 83

## Slide 60: Lyapunov stability concept for linear systems
▶ for linear system = Ax , a good Lyapunov candidate is the quadratic function V (x ) = x T Px where P = PT and P ≻ 0
▶ the derivative along the state trajectory is then
(x ) = T Px + x T P
= (Ax )T Px + x T PAx
= x T (AT P + PA) x
▶ such a V (x ) = x T Px is a Lyapunov function for = Ax when
AT P + PA ⪯ 0
▶ and the origin is stable in the sense of Lyapunov
Stability
60 / 83

## Slide 61: Theorem (Lyapunov stability theorem for linear systems)
For = Ax with A ∈ Rn×n, the origin is asymptotically stable if and only if for any symmetric positive definite matrix Q ≻ 0, the Lyapunov equation
AT P + PA = −Q
has a unique positive definite solution P ≻ 0, PT = P.
Stability
61 / 83

## Slide 62: Essense of the Lyapunov Eq.
Observations:
▶ AT P + PA is a linear operation on P: e.g.,
AT p1 + a11p1 + a21p2 = −q1
AT p2 + a12p1 + a22p2 = −q2
Stability
62 / 83

## Slide 63: Essense of the Lyapunov Eq.
T
A P + PA = Q ⇔
Observations: with now
T
A p + a
p + a p
1 11 1 21 2
= −q1
2 12 1 22 2
AT p + a p + a p = −q
2
▶ can stack the columns of AT P + PA and Q to yield
Stability
63 / 83

## Slide 64: The Lyapunov Eq.: Existence of solution
L u u = u u A + A u
LA (P) = AT P + PA
▶ LA is invertible if and only if λi + λj 0 for all eigenvalues of A:
▶ let AT ui = λiui and AT uj = λjuj
▶
A i
j
( )
j
T T T
i i
T
j
T
i j j i i
T
j
u = u (λ u ) + λ u u =
(λi + λj ) uiuT
j
▶ so λi + λj is an eigenvalue of the operator LA (·)
▶ if λi + λj 0, the operator is invertible
Stability
64 / 83

## Slide 65: The Lyapunov operator: eigenvalues
▶ can simply write LA = I ⊗ AT + AT ⊗ I using the Kronecker
Stability
mirror symmetric
product notation B ⊗ C =

## Slide 66: The Lyapunov operator: eigenvalues
▶ e.g., A =
LA = I ⊗ AT + AT ⊗ I =
= =
Stability

## Slide 67
Stability
67 / 83
Example: A = ,
The eigenvalues of LA are , which are precisely λ1 + λ1, λ1 + λ2, λ2 + λ1, λ2 + λ2.
import numpy as np
A = [[-1,1],[-1,0]]; I2=np.eye(2); AT=np.transpose(A) L_A=np.kron(I2,AT)+np.kron(AT,I2) eigLA,_=np.linalg.eig(L_A)
eigA,_=np.linalg.eig(A) print(eigLA)
print(eigA)
LA = I ⊗ AT + AT ⊗ I =

## Slide 68: Theorem (Lyapunov stability theorem for linear systems)
For = Ax with A ∈ Rn×n, the origin is asymptotically stable if and only if for any symmetric positive definite matrix Q ≻ 0, the Lyapunov equation
AT P + PA = −Q
has a unique positive definite solution P ≻ 0, PT = P.
Proof.
P ≻ 0 ⇒ (λQ )min > 0 and (λP )max > 0. Thus α > 0; V (t) decays
exponentially to zero. V (x ) ≻ 0 ⇒V (x ) = 0 only at x = 0. Therefore, x → 0 as t → ∞, regardless of the initial condition.
Stability
68 / 83
“⇒”:
−αt
⇒ V (t) ≤ e V (0).
Q ≻ 0 and

## Slide 69: Proof.
Stability
69 / 83
“⇐”: if 0 of =Ax is asymptotically stable, then all eigenvalues of A have negative real parts. For any Q, the Lyapunov equation has a unique solution P. Note x (t) = eAtx0 → 0 as t → ∞. We have
T
If Q ≻ 0, there exists a nonsingular N matrix: Q = N N. Thus
Thus P ≻ 0. Furthermore
only if
0

## Slide 70: Procedures of Lyapunov’s direct method
Given A, select an arbitrary positive-definite symmetric matrix Q
(e.g., I ).
Find the solution matrix P to the Lyapunov equation
AT P + PA = −Q.
If a solution P cannot be found, the origin is not asymptotically stable.
If a solution is found:
▶ if P is positive-definite, then A is Hurwitz stable and the origin is asymptotically stable;
▶ if P is not positive-definite, then A has at least one eigenvalue with a positive real part and the origin is an unstable equilibrium.
Stability
70 / 83

## Slide 71: Lyapunov stability theorems
11 11 22
2
12
Leading principle minors: p > 0, p p − p > 0
⇒ P ≻ 0 ⇒asymptotically stable
Stability
71 / 83
Example
. The Lyapunov equation is
We need

## Slide 72
Lyapunov analysis with Matlab
Stability
.
A = [-1,1;-1,0]
Q = eye(2)
P = lyap(A’,Q) w = eig(P)

## Slide 73
Lyapunov analysis with Python
Stability
import control as ct import numpy as np
A = np.array([[-1,1],[-1,0]])
Q = np.identity(2)
P = ct.lyap(A.transpose(),Q) print(P)
w = np.linalg.eigvals(P) print(f’eigenvalues of P: {w}’)
.

## Slide 74: It suffices to select Q = I
For linear systems we can let Q = I and check whether the resulting P is positive definite. If it is, then we can assert the asymptotic stability:
▶ take any Q ≻ 0. there exists Q = NT N, where N is invertible, yielding
AT P + PA = −I
⇕
▶ = N−1AN and A are similar matrices and have the same eigenvalues.
▶ P˜ = NT PN and P have the same definiteness. If we can find a positive definite solution P then the P˜ will also be positive definite. Vise versa.
Stability
74 / 83

## Slide 75: Instability theorem
▶ for nonlinear systems, Lyapunov function can be nontrivial to find
▶ failure to find a Lyapunov function does not imply instability
Theorem
The equilibrium state 0 of = f (x ) is unstable if there exists a function W (x ) such that
▶ W˙ (x ) is PD locally: W˙ (x ) > 0 ∀ |x | < r for some r and
W˙ (0) = 0
▶ W (0) = 0
▶ there exist states x arbitrarily close to the origin such that
W (x ) > 0
Stability
75 / 83

## Slide 76: Discrete-time case: key concept of Lyapunov
For the discrete-time system
x (k + 1) = Ax (k)
we consider a quadratic Lyapunov function candidate
V (x ) = x T Px, P = PT ≻ 0
and compute ∆V (x ) along the trajectory of the state
Stability
76 / 83
V (x (k + 1)) − V (x (k)) = x T (k) x (k)
Asymptotic stability desires ∆V (x ) to be negative.

## Slide 77: DT Lyapunov stability theorem for linear systems
Theorem
For system x (k + 1) = Ax (k) with A ∈ Rn×n, the origin is asymptotically stable if and only if ∃ Q ≻ 0, such that the discrete-time Lyapunov equation
AT PA − P = −Q
has a unique positive definite solution P ≻ 0, PT = P.
Stability

## Slide 78: The DT Lyapunov Eq.
AT PA − P = −Q
▶ Solution to the DT Lyapunov equation, when asymptotic stability holds (A is Schur stable), comes from:
▶ can show that the DT Lyapunov operator LA = AT PA − P is invertible if and only if ∀i, j (λA)i (λA)j 1
Stability
78 / 83
0

## Slide 79
DT Lyapunov analysis with MATLAB
Example
x (k + 1) = Ax (k), A =
0
1
0
0 0 1
0.275 −0.225 −0.1
Stability
% MATLAB
A=[ 0 1 0; 0 0 1; 0.275 -0.225 -0.1]
Q = eye(3)
P = dlyap(A’,Q) % check function definition in Matlab help eig(P)

## Slide 80
DT Lyapunov analysis with Python
Example
x (k + 1) = Ax (k), A =
0
1
0
0 0 1
0.275 −0.225 −0.1
Stability
#Python import control as ct import numpy as np from numpy.linalg import eig A = np.array([[0,1,0],[0,0,1],[0.275,-0.225,-0.1]]) Q = np.identity(3) P = ct.dlyap(A.transpose(),Q) w,v = eig(P) print(w)

## Slide 81: Recap
▶ Internal stability
▶ Stability in the sense of Lyapunov: ε, δ conditions
▶ Asymptotic stability
▶ Stability analysis of linear time invariant systems (= Ax or
x (k + 1) = Ax (k))
▶ Based on the eigenvalues of A
▶ Time response modes
▶ Repeated eigenvalues on the imaginary axis
▶ Routh’s criterion
▶ No need to solve the characteristic equation
1−s
▶ Discrete time case: bilinear transform (z = 1+s )
Stability

## Slide 82: Recap
▶ Lyapunov equations
Theorem: All eigenvalues of A have negative real parts iff for any given Q ≻ 0, the Lyapunov equation
AT P + PA = −Q
has a unique solution P and P ≻ 0.
Given Q, the Lyapunov equation AT P + PA = −Q has a unique solution when λA,i + λA,j 0 for all i and j.
Theorem: All eigenvalues of A are inside the unit circle iff for any given Q ≻ 0, the Lyapunov equation
AT PA − P = −Q
has a unique solution P and P ≻ 0.
Given Q, the Lyapunov equation AT PA − P = −Q has a unique solution when λA,iλA,j 1 for all i and j.
Stability

## Slide 83: Recap
▶ P is positive definite if and only if any one of the following conditions holds:
All the eigenvalues of P are positive.
All the leading principle minors of P are positive.
There exists a nonsingular matrix N such that P = NT N.
Stability